## Slide 1: Hyperdimensional Computing for Noninvasive Brain–Computer Interfaces: Blind and One-Shot Classification of EEG Error-Related Potentials
Abbas Rahimi, Pentti Kanerva, José del R. Millán, Jan M. Rabaey
EECS Department, UC Berkeley
IBI-STI, EPFL

## Slide 2: Outline
Architecture for Brain-Computer Interface (BCI)
  Electroencephalogram (EEG) error-related potentials
Hyperdimensional Computing Basics
  Mapping to hypervectors and arithmetic
  Hyperdimensional computing examples
Mapping EEG Electrodes to Hypervectors
Temporal-Spatial Hyperdimensional Encoder
Experimental Results
Summary

## Slide 3: General Architecture for Brain-Computer Interface (BCI)
Goal: Using a brain-inspired computing model—hyperdimensional computing— to understand brain signals!
Hyperdimensional Computing
64 electrodes
Two classes

## Slide 4: EEG Error-Related Potentials
To classify EEG ERPs:
  Baseline: spatial CAR preprocessing, per-subject selective electrodes, and statistical Gaussian model [Chavarriaga, et al, TNSRE’10]
  Our work: brain-inspired hyperdimensional computing
    Less preprocessing (no CAR filter)
    Blindly using all electrodes (no prior domain expert knowledge)
    Faster learning
Error-related potential (ERP) as a backseat driver!
A user monitors the performance of an external agent upon which the user has no control
User provides no commands, but only monitors the agent's performance.
CAR: Common Average Reference

## Slide 5: Experimental Protocol of ERPs
Red square as target location
Green square as moving cursor
Dotted square as cursor location at the previous time step
At each trial the cursor moves horizontally to reach the target
The probability of moving in the wrong direction is ~0.2
t
Start
t+1
Correct move
t+2
Wrong move
2000 ms

## Slide 6: Brain-inspired Hyperdimensional Computing
Hyperdimensional (HD) computing [P. Kanerva, Cognitive Computation’09]:
Emulation of cognition by computing with high-dimensional vectors as opposed to computing with numbers
Information distributed in high-dimensional space
The algebra of hypervectors leads to a powerful model of computing
Superb properties:
General and scalable model of computing
Well-defined set of arithmetic operations
Fast and one-shot learning (no need of back-prop)
Memory-centric with embarrassingly parallel operations
Extremely robust against most failure mechanisms and noise
Our aim is to develop an efficient and fast learning method based on HD computing to blindly operate with all electrodes and with raw data.

## Slide 7: What Are Hypervectors?
  Distributed pattern–based data representations and arithmetic in contrast to computing with numbers!
Hypervectors are:
  high-dimensional (e.g., 10,000 dimensions)
  (pseudo)random with i.i.d. components
  holographically distributed (i.e., not microcoded)
Hypervectors can:
  use various coding: dense or sparse, bipolar or binary
  be combined using arithmetic operations: multiplication, addition, and permutation (MAP)
  be compared for similarity using distance metrics, e.g., Hamming distance

## Slide 8: Mapping to Hypervectors
Each “symbol” (e.g., a channel in EEG) is represented by a 10,000−D hypervector chosen at random:
N1 = [−1 +1 −1 −1 −1 +1 −1 −1 ...]
N2 = [+1 −1 +1 +1 +1 −1 +1 −1 ...]
N3 = [−1 −1 −1 +1 +1 −1 +1 −1 ...]
N4 = [−1 −1 −1 +1 +1 −1 +1 −1 ...]
...
N64 = [−1 −1 +1 −1 +1 +1 +1 −1 ...]
Every hypervector is dissimilar to others, e.g., ⟨N1, N2⟩ = 0
This assignment is fixed throughout computation
Item Memory (iM)
‘Fp1’
N1
6
10,000

## Slide 9: HD Arithmetic
Addition (+) is good for representing sets, since sum vector is similar to its constituent vectors.
  ⟨A+B, A⟩=0.5
Multiplication (*) is good for binding, since product vector is dissimilar to its constituent vectors.
  ⟨A*B, A⟩=0
Permutation (ρ) makes a dissimilar vector by rotating, it is good for representing sequences.
  ⟨A, ρA⟩=0

## Slide 10: Its Algebra is General: Architecture Can Be Reused
Associative memory
S1
5-bit
10K-bit
Item memory
10K-bit
Hand gestures: 5 classes
S2
5-bit
10K-bit
Item memory
S3
5-bit
10K-bit
Item memory
S4
5-bit
10K-bit
Item memory
Encoder: MAP operations
Associative memory
Letter
8-bit
10K-bit
10K-bit
Languages: 21 classes
Item memory
Encoder: MAP operations
Applications | n-grams | HD | Baseline
Language identification [ISLPED’16] | n=3 | 96.7% | 97.9%
Text categorization [DATE’16] | n=5 | 94.2% | 86.4%
EMG gesture recognition [ICRC’16] | n∈ [3,5] | 97.8% | 89.7%
EEG brain-machine interface [BICT’17] | n∈ [16,29] | 74.5% | 69.5%

## Slide 11: Mapping an EEG Electrode to Hypervectors
Item Memory (iM) maps channels to orthogonal hypervectors.
Continuous iM (CiM) maps quantities continuously to hypervectors.
value
CiM
Quantization: 100 levels
‘Fp1’
name
iM
Fp1

## Slide 12: Temporal HD Encoder for one EEG Electrode
CiM contains 100 hypervectors for continuous mapping (2 orthogonal hypervectors)
iM contains 64 orthogonal hypervectors, one per electrode
Temporal Encoder:
  Rotate (ρ) a signal level to capture its history producing a temporal n-gram (G1)
  Bind an electrode name (e.g., N1) to its temporal n-gram: N1 * G1
  This binding produces a record R1 describing the electrode of interest
Preprocessing
BPF
iM
level
CiM
mean
Quant 100
‘Fp1’
name
1st Electrode
Fp1
R1
*
N1
*
Temporal Encoder
…
ρ
L1,n
ρ
L1,3
ρ
L1,2
L1,1
G1

## Slide 13: Temporal-Spatial HD Encoder
R1
Preprocessing
BPF
iM
level
CiM
*
mean
Quant 100
‘Fp1’
name
1st Electrode
Fp1
N1
*
Temporal Encoder
…
ρ
L1,n
ρ
L1,3
ρ
L1,2
L1,1
G1
+
E
Spatial
Encoder
… …. …
O2
*
Temporal Encoder
…
ρ
L64,n
ρ
L64,3
ρ
L64,2
L64,1
R64
Preprocessing
BPF
iM
level
CiM
*
mean
Quan 100
‘02’
name
N64
G64
64th Electrode
Generate a temporal-spatial hypervector across 64 electrodes by addition

## Slide 14: Class Prototypes in Associative Memory
Temporal-Spatial Encoder
W
C
Cosine
?+
?+
E
“correct”/”wrong”
Associative Memory
Fp1
O2
…
for : if then
if then
HD computing shares the same structure for both training and testing!

## Slide 15: Fast and One-shot Learning
Training with only 2.6% of the total non-redundant trials:
  HD accuracy reaches to 79.3% (higher than the baseline using all training trials).

## Slide 16: Fast and One-shot Learning by 6 Subjects
HD classifier learns faster: it uses only 0.3% of the non-redundant training trials for S6, and up to 96% for S1.
On average, HD classifier meets the target accuracy of 70% when trained with only 34% of non-redundant training trials.

## Slide 17: Blindly Using All Electrodes w/o Preprocessing
Compared to baseline:
Using the same setup: HD has 5% higher accuracy
Using all electrodes w/o CAR filter: HD has 2.2% higher accuracy

## Slide 18: Summary
An application of HD computing to the classification of error-related potentials from EEG recordings
Classification of EEG error-related potentials is comparable to the baseline classifier crafted by a skilled professional:
  HD algorithm does the classification without requiring prior knowledge about the important channels for this task; HD uses all 64 channels while baseline selectively uses 1 or 2 channel(s) based on the subject
  HD algorithm uses lighter preprocessing (no CAR filter)
  HD achieves this task with fewer training data
Open source HD code: https://github.com/abbas-rahimi/HDC-EEG-ERP

## Slide 19: Acknowledgment
This work was supported in part by
Systems on Nanoscale Information fabriCs (SONIC), one of the six SRC STARnet Centers, sponsored by MARCO and DARPA
Intel Strategic Research Alliance (ISRA) program on Neuromorphic Architectures for Mainstream Computing