## Slide 1: ARGO: Aging-aware GPGPU Register File Allocation
Majid Shoushtari
Nikil Dutt
Puneet Gupta
Computer Science
Electrical Engineering
http://variability.org
Computer Science and Engineering
Abbas Rahimi
Rajesh Gupta

## Slide 2: The Future is Heterogeneous Computing
Slide borrowed from AMD keynote in ISSCC 2013

## Slide 3: CPU+GPU Integration in Mobile SoCs
Slide borrowed from NVIDIA

## Slide 4: What’s the problem?
To support highly parallel execution, GPGPUs contain large RFs
  NVIDIA GTX480: 2MB
  AMD Radeon HD5870: 5MB
Aging mechanisms are becoming one of the most pressing sources of circuit variations as technology shrinks.
Large RFs are being threatened by Aging

## Slide 5: Outline
Background on NBTI
Related Work
GPGPU Architectural Model
Observation: RF Underutilization
ARGO
Experimental Results

## Slide 6: NBTI: A Major Aging Mechanism
Negative Bias Temperature Instability has emerged as a major reliability problem in current and future technology generations.
NBTI manifests itself as a shift in Vth
  Logic: Slower circuit  Timing Error
  Memory: Reduced “Signal to Noise Margin”
Recovery effect in periods of no stress
  Full recovery from a stress period only possible in infinite time
  In practice overall Vth shift increases monotonously
Higher Temperature  Faster Aging
NBTI makes the memory cell unstable.
Existing Strategies:
1) Higher Vdd (guardband) required; or
2) Life-time decreased by NBTI
ARGO:
Increase Life-time without Vdd guardband

## Slide 7: Related Work
RF/Caches
  Wearout-aware register allocation [Ahmed’12]
  Exploiting RF underutilization for power saving [Tabkhi’12]
  Partitioned cache for reducing NBTI-induced aging [Calimera’11]
GPGPUs
  Aging in functional units of GPGPU [Rahimi’13]
No work on aging of RFs for
multi-threaded GPGPUs

## Slide 8: GPGPU Architecture & Execution Model: AMD Evergreen
Radeon HD 5870 (5 MB RF)
  20 Compute Units (CUs)
    16 Stream Cores (SCs) per CU (SIMD execution)
      5 Processing Elements (PEs) per SC (VLIW execution)
      16 KB Register File per SC
Ultra-threaded Dispatcher
Compute Unit (CU0)
Compute Unit (CU19)
L1
L1
Crossbar
Global Memory Hierarchy
Compute Device
SIMD Fetch Unit
Stream Core
(SC0)
Stream Core (SC15)
Local Data Storage
Wavefront Scheduler
Compute Unit (CU)
T
General-purpose Reg.
X
Y
Z
W
Branch
Processing Elements (PEs)
Stream Core (SC)
X
Y
Z
W
.
.
.
16 KB
.
.
.
ND-Range
WG
WG
WG
WG
…
.
.
.
.
.
.
…
Work-Group
WI
WI
WI
WI
…
.
.
.
.
.
.
…
Common OpenCL Kernel:
_kernel func()
{
}
Work-Item

## Slide 9: Observation: RF Underutilization
Resources are fixed per compute unit
  local memory size
  maximum number of threads
  number of registers
Any one of these resource constraints
may limit #WG / CU ≡ occupancy
Kernel | #of Registers | RF Utilization
Reduction | 4 | 50%
BinarySearch | 2 | 25%
DwtHaar1D | 4 | 50%
BitonicSort | 4 | 13%
FastWalshTransform | 4 | 50%
FloydWarshall | 6 | 75%
BinomialOption | 13 | 81%
DiscreteCosineTransform | 7 | 22%
MatrixTranspose | 3 | 38%
MatrixMultiplication | 22 | 69%
SobelFilter | 9 | 99%
URNG | 6 | 19%
RadixSort | 16 | 6%
Histogram | 16 | 13%
BlackScholes | 19 | 89%
This characteristic is preserved across set of OpenCL compiler options
On average 54% of RF is not utilized at all
Opportunistically exploiting RF
underutilization for NBTI recovery

## Slide 10: ARGO: Overall Approach
Detect aging (which RF banks are stressed?)
  Use “Virtual Sensor” to predict stressed banks
Distribute stress in RFs
  Perform leveling (rotating allocation) of RFs
Power gate stressed RF banks
  Allow stressed RF banks to recover

## Slide 11: Sliced RF Organization
RF is partitioned into 16 Slices
Each slice serves one SC
RF is horizontally banked into 256 banks
Each bank is 1KB and has separate power domain
Each bank serves one WF
RF is allocated at granularity of WG
Dispatcher maps a WG to an available CU
RF allocator assigns a portion of RF to WG
WG + head of allocated space will be inserted into scheduler queue
Logical Address
Physical Address
WG #
+
WI #
+
Allocated RF Head

## Slide 12: Baseline (Aging Oblivious) RF Allocation
Kernel | #Reg. | Limited by | #WF per WG | #WG per CU | #Bank required | RF Utilization
Reduction | 4 | Max # of threads | 4 | 8 | 4*8*4 = 128 | 128/256 = 50%
16 banks
256 banks
WG1
WG2
WG3
WG4
WG5
WG6
WG7
WG8
WG9
WG10
WG13
WG11
WG14
WG15
WG16
WG12
Low-indexed RF banks are stressed more

## Slide 13: ARGO: RF Allocation
WG1
WG2
WG3
WG4
WG5
WG6
WG7
WG8
Distributing stress by rotating allocated RF portions
Healing
Level
WG9
WG10
WG13
WG11
WG14
WG15
WG16
WG12
Recovery

## Slide 14: ARGO: Overview
Aging Instrumentation options
  NBTI Sensors
    Area and Power Overhead
  Light-weight Virtual Sensing
    Estimating Aging Profile of RF Portions in Relative Manner
Modifying RF Allocator + Adding RF Power-gators

## Slide 15: ARGO: Virtual Sensing
Ultra-threaded dispatcher doesn’t allocate different type of kernels to a CU at a time.
Observation: Variation in execution time of different WG of a kernel is < 8% for a wide range of kernels. Why?
  Round-robin WF scheduler.
  Strategy that GPGPUs follow handling thread divergence.

## Slide 16: ARGO: Virtual Sensing (cont.)
RF portions are allocated per WG.
All cells within a RF portion are aged at the same rate.
At WG granularity, RF banks aged at the same rate
  Why? Because all are under stress for near-constant amount of time.
Least-degraded portion of RF is least-recently-allocated portion

## Slide 17: ARGO: RF Allocator
Based on Virtual Sensing:
  One rotation per each new WG
    Guarantees greedily allocating least-recently-allocated (= least-degraded) RF portion
Issues proper power-gating signals
  Primary goal is recovery
  Side benefit is opportunistic saving of leakage power for unused banks

## Slide 18: ARGO: Overheads
Overheads imposed by ARGO’s micro-architectural modifications?
  Performance:
    No performance overhead thanks to single-cycle implementation of ARGO RF allocator, similar to baseline RF allocator
  Area:
    <1% of RF area
  Power:
    < 0.5% of leakage power of RF
Overheads are negligible

## Slide 19: Experimental Setup
Multi2Sim
  A cycle-accurate simulation framework − a CPU-GPU model for heterogeneous computing targeting AMD Evergreen ISA
Kernels of AMD APP SDK 2.5
  Large parameters to put highest load on resources
HSPICE for SNM measurements

## Slide 20: Simulation Result: Vth Shift
On average 27% improvement in Vth shift
Normalized to reduction in baseline mode
~100% RF utilization, no opportunity for recovery
No improvement, but no performance degradation too
Min Improvement: 10%
Max Improvement:
43%

## Slide 21: Simulation Result: SNM Degradation
Chart: Reduction in SNM Degradation
| Rdn | BSe | DH1D | BSo | FWT | FW | BO | DCT | MT | MM | SF | URNG | RS | HS | BSc
45nm | 0.26866 | 0.32463 | 0.25373 | 0.45149 | 0.28731 | 0.20149 | 0.13433 | 0.38806 | 0.29851 | 0.16791 | 0 | 0.41045 | 0.44403 | 0.39179 | 0.11194
Improvements in SNM and Vth show the same trend as expected [23]
On average 30% improvement in SNM

## Slide 22: Simulation Result: Trend of SNM Degradation
Unsafe Zone
Aging-Oblivious Trend
Depending on tech. and init. SNM, 15% to 20% reduction in SNM makes SRAM unreliable
Entrance to “Unsafe Zone” shifted from 0.7 to 1.45
All curves below 20%
after 5 years of execution

## Slide 23: Summary
Aging is becoming a reliability threat
GPGPUs have large RFs susceptible to aging
Observation: GPGPU RF utilization is ~46%
ARGO: Key Ideas
  Exploit RF underutilization
  Overcome aging by leveling (rotating) allocation of stressed RFs
ARGO improves SNM by 30% on average.
Please come to our poster for more details

## Slide 24: Thank you
Q&A
NSF Expedition in Computing, Variability-Aware Software for Efficient Computing with Nanoscale Devices http://variability.org

## Slide 25: Supplementary Slides

## Slide 26: Simulation Result: Recovery / Bank Size Tradeoff
Kernel | Recovery Time (%) |  |  | 
 | 1K | 2K | 4K | 8K
Rdn | 48% | 48% | 48% | 48%
BSe | 63% | 63% | 63% | 63%
DH1D | 44% | 44% | 44% | 44%
BSo | 87% | 87% | 87% | 87%
FWT | 53% | 53% | 53% | 53%
FW | 29% | 29% | 29% | 29%
BO | 13% | 13% | 13% | 8%
DCT | 77% | 73% | 73% | 73%
MT | 56% | 56% | 56% | 42%
MM | 21% | 21% | 14% | 14%
SF | 0% | 0% | 0% | *
URNG | 81% | 81% | 75% | 75%
RS | 86% | 86% | 86% | 86%
HS | 78% | 78% | 78% | 78%
BSc | 9% | 9% | 9% | 4%
8K bank results in performance degradation
Bank Size
Overhead of power-gating logic can be reduced by coarser bank size
WF per WG × #of registers is already a multiple of bank size.
2K or 4K banks are near optimal

## Slide 27: Simulation Result: Different Process Corners
Chart: Improvement in Read SNM
| 0.9V - 25°C | 0.9V - 110°C | 1V - 25°C | 1V - 110°C
Year 1 | 0.20408 | 0.38385 | 0.19298 | 0.38622
Year 2 | 0.2 | 0.38574 | 0.21538 | 0.38863
Year 3 | 0.18966 | 0.38731 | 0.2029 | 0.39051
Year 4 | 0.19672 | 0.38797 | 0.20548 | 0.39118
Year 5 | 0.20312 | 0.38903 | 0.21053 | 0.39136
Gain is almost constant over the years
Temp. constant, varying Voltage
Voltage constant, varying Temp.