## Slide 1: Aging-Aware Compiler-Directed VLIW Assignment for GPGPU Architectures
Variability.org
Abbas Rahimi‡, Luca Benini†, Rajesh K. Gupta‡
‡UC San Diego, †University of Bologna
Micrel.deis.unibo.it
/MultiTherman
Aging-Aware Compiler-Directed VLIW Assignment for GPGPU Architectures
Aging-Aware Compiler-Directed VLIW Assignment for GPGPU Architectures
Aging-Aware Compiler-Directed VLIW Assignment for GPGPU Architectures

## Slide 2: Variability is about Cost and Scale
Variability in transistor characteristics is a major challenge in nanoscale CMOS:
  Static Process variation: Leff and Vth
  Dynamic variations: Temperature fluctuations, supply Voltage droops, and device Aging (NBTI, HCI)
To handle variations designers use conservative guardbands  loss of operational efficiency 
Clock
actual circuit delay
Process
Temperature
Aging
VCC Droop
guardband
NBTI-induced performance degradation
∆VTH = F (Process, Temp, Voltage, Stress)
Stress consumes timing margin.
Stress (workload)
VTH
Operational
Failure
guardband
Lifetime is limited by the most aged component.
Complicated with 512 CUDA cores, or 320 5-way VLIW cores!
∆Vth
∆P


## Slide 3: Related Work
NBTI-aware power-gating exploits the sleep state where a circuit is inherently immune to aging [Calimera’09, Calimera’12]
  High power-gating factors impose performance degradation 
Equalize the stress among various functional units in single-core [Gunadi’10]
  They intrusively modified pipeline to support complement mode execution and operand swapping 
Traditional coarse-grained multi-core utilize selective voltage scaling [Tiwari’08, Karpuzcu’09]
  Difference between adaptive voltage and over-designed voltage is small 
Process variation in GPGPU [Lee’11]
  Disabling the slowest cores! 
  Cannot capture the aging which is dynamic in nature!

## Slide 4: Contribution
Aging-aware compiler that utilizes a dynamic binary optimizer for customizing the kernels code to respond to the specific health state of hardware:
  Specific health state (online NBTI sensors)
  Uniformly distributes the stress of instructions among various VLIW slots, results in a healthy code generation.
An adaptive reallocation strategy, a fully software solution, without any architectural modification with iso-throughput kernels:
  Throughput (healthy kernel) = Throughput (naïve kernel)

## Slide 5: AMD Evergreen GPGPU Architecture
Radeon HD 5870
  20 Compute Units (CUs)
    16 Stream Cores (SCs) per CU (SIMD execution)
      5 Processing Elements (PEs) per SC (VLIW execution)
        4 Identical PEs (PEX, PEY, PEW, PEZ)
        1 Special PET
Ultra-threaded Dispatcher
Compute Unit (CU0)
Compute Unit (CU19)
L1
L1
Crossbar
Global Memory Hierarchy
Compute Device
SIMD Fetch Unit
Stream Core (SC0)
Stream Core (SC15)
Local Data Storage
Wavefront Scheduler
Compute Unit (CU)
T
General-purpose Reg
X
Y
Z
W
Branch
Processing Elements (PEs)
Stream Core (SC)
X : MOV R8.x, 0.0f
Y : AND_INT T0.y, KC0[1].x
Z : ASHR T0.x, KC1[3].x
W:________
T:_________
ILPVLIW
Packing ratio = 3/5

## Slide 6: GPGPU Workload Variation
✓
✓
×
Uniform workload variation between CUs: 0%−0.26%
Load balancing algorithm of the ultra-thread dispatcher 
Inter-compute units
Inter-stream cores
Inter-processing elements
SIMD Execution 
T
General-purpose Reg
X
Y
Z
W
Branch
Processing Elements (PEs)
Stream Core (SC)
Ultra-threaded Dispatcher
Compute Unit (CU0)
Compute Unit (CU19)
L1
L1
Crossbar
Global Memory Hierarchy
Compute Device
SIMD Fetch Unit
Stream Core (SC0)
Stream Core (SC15)
Local Data Storage
Wavefront Scheduler
Compute Unit (CU)
50%
Instructions are NOT uniformly distributed among PEs !!
Seven kernels execute more than 40% of the ALU engine instructions only on PEX 
Compiler only increases the packing ratio  weighted VLIW code generation is needed
We leverage an average packing ratio of 0.3 towards reliability improvement!
Finding N-young slots among all available slots

## Slide 7: Aging-Aware Compilation Flow
GPGPU
Dynamic Binary Optimizer
Host CPU
Naïve Kernel
Healthy Kernel
5-Way VLIW Bundle
Limited Packing Ratio
NBTI Sensors
Periodic healthy kernels generation:
1. “Fatigued” PEs are relaxing!
2. “Young” PEs are working hard!
Non-uniform Inst. Distribution
Uniform VLIW Assignment
Static Code Analysis
X : MOV …
Y : ASHR …
Z :_________
W:________
T:_________
X :_________
Y :_________
Z : MOV …
W: ASHR …
T:_________
Leveling of slots
Equalizes the expected lifetime of each PEs

## Slide 8: Experimental Results
VTH = 406mV
uniform ∆VTH=0.6mV
Process variation and NBTI-induced for 360 hours without power gating in HD 5870.
Periodically the execution of healthy kernels, compared to the naïve kernels
  Reduces Vth shift up to 49%(11%) and on average 34%(6%) in presence(absence) of power-gating supports
  Imposes 0% throughput penalty (maintaining the naïve ILP)
Inter-PEs ∆VTH=10mV
VTH = 413mV
Extended lifetime 

## Slide 9: Conclusion
An adaptive compiler-directed technique that uniformly distributes the stress of instructions throughout various VLIW resource slots.
Equalizing the expected lifetime of each processing element by regenerating aging-aware healthy kernels that respond to the specific health state of GPGPU while maintaining iso-throughput execution.
Work in progress
  Memory subsystems: reducing Vth shift by up to 43% for register files of GPGPU.
Thank you!

## Slide 10: Aging-aware Kernel Adaptation Flow
Aging-aware Slot Assignment
Healthy Code Generation
τ{X,…,W} [t]
∆τ{X,…,W} [t+1]
Just-in-time Disassembler
Static Code Analysis
Device-dependent Assembly Code
∆Vth−{X,…,W} [t+1]
Linear Calibration
∆Vth−{X,…,W}[t]
NBTI
Sensors Banks
GPGPU Compute Device
Input
Output
Kernel
Memory Mapped Sensors
Memory
Naïve Kernel Binary
Healthy Kernel Binary
Host CPU
Rank | Vth | τ
Age[1] | Vth-X [t] | τX [t]
Age[2] | Vth-Y [t] | τY [t]
… | … | …
Rank | ∆Vth | ∆τ
Util[1] | ∆Vth-Y [t+1] | ∆τY [t+1]
Util[2] | ∆Vth-Z [t+1] | ∆τZ [t+1]
… | … | …
Wearout
Estimation
Module
Pred-∆Vth−{X,…,W}[t+1]
Performance
Degradation
Measurement
1
2
3
4
Naïve Kernel
Reading sensors measurements
Static code analysis technique estimates the percentage of instructions that will carry out on every PE (a linear calibration module later fits the predicted ∆VTH shift to the observed ∆VTH shift).
Finally, the uniform slot assignment assigns fewer/more instructions to higher/lower stressed slots.
Healthy kernel binary 

## Slide 11: Total execution time of adaptation flow
Average execution time of the entire process, starting from disassembler up to the healthy code generation.
  Kernel disassembly using online CAL (95% total time)
  Static code analysis: 220K−900K cycles
  Uniform slot assignment algorithm ≤ 2K cycles
On average 13 millisecond on a host machine with an Intel i5 2.67GHz

## Slide 12: AMD APP SDK 2.5 kernels with parameters
Kernel | Parameter
Reduction (Rdn) | N= 100,000
BinarySearch (BSe) | N= 10,000
DwtHaar1D (DH1D) | N= 10,000
BitonicSort (BSo) | N= 1,000
FastWalshTransform (FWT) | N= 1,000
FloydWarshall (FW) | N= 100
BinomialOption (BO) | N= 100
DiscreteCosineTransform (DCT) | X= 500 Y= 500
MatrixTranspose (MT) | X= 300 Y= 300
MatrixMultiplication (MM) | X= 300 Y= 300 Z= 300
SobelFilter (SF) | default input file
URNG | default input file