## Slide 1
Task Scheduling Strategies to Mitigate Hardware Variability in Embedded Shared Memory Clusters
Abbas Rahimi Rajesh K. Gupta UC San Diego
Andrea Marongiu Luca Benini ETH Zurich
Daniele Cesarini
University of Bologna

## Slide 2: Key Idea
Time or part
Cost
Application
Application
OpenMP Runtime
Reduced
Cost
Efficient
Runtime
Efficient error recovery in runtime software

## Slide 3: Outline
Background about Variability
Related Work
Contributions
Target Architecture Platform
Online Meta-data Characterization
Scheduling
  Centralized
  Distributed
Experimental Results
Summary

## Slide 4: Ever-increasing Variability in Semiconductor
Technology Generation (nm)
Performance
130 90 65 45 32 22 post-silicon
design for worst case
scaling
~20× performance variation in near threshold!
Guardbanding leads to loss of operational efficiency!
< 10%
> 50% [ITRS]
Guard-
banding

## Slide 5: Reduced Guardband Causes Timing Error
Reducing guardband
Timing error
Costly error recovery
3×N recovery cycles per error for an in-order pipeline!
N = number of stages
Grand challenge: low-cost and scalable variability-tolerance
[Bowman, JSSC’09]
[Bowman, JSSC’11]

## Slide 6: Related Work
HW
SW
Scheduler/ Allocator
Work units
Tasks
Sequence
ISA
ISA vulnerability [DATE’12]
Improved code transformation [ASPLOS’11, TC’13]
Coarse-grained task/thread scheduling [JSSC’11]
Task-level tolerance [DATE’13]
Work-unit tolerance [JETCAS’14]
Instruction replay [JSSC’11]
OpenMP captures variations in various parallel software context!

## Slide 7: Contributions
Reducing the cost of recovery by exposing errors to runtime layer of OpenMP
Online meta-data characterization to capture variation (per core) and workload  Task execution cost
Scheduling policies
  Centralized
  Distributed

## Slide 8: Target Architecture Platform
CPU
MMU
L2 $
Coherent interconnect
L1 $
…
Interconnect
cluster
L2 mem
IO MMU
L1 mem
…
Cluster
L1 mem
NI
Main memory
Host
Cluster-based many-core
Core 0
L1 I$
…
Core 15
L1 I$
NI
Low-latency Interconnect
BANK 1
BANK 2
BANK 32
…
DMA
Shared memory cluster
L1 DATA mem (TCDM)
…
Stage 1
Stage 2
Stage 7
Core
ΣI
EDAC
ΣIR
Shared memory cluster:
16 32-bit in-order RISC processors
Shared L1 tightly-coupled data memory (TCDM)
Each core uses EDAC with multiple-issue instruction replay

## Slide 9: Online Meta-data Characterization
ApplicationX:
#pragma omp parallel { #pragma omp master {
for (int t = 0; t < Tn; t++) #pragma omp task
run_add (t, TASK_SIZE);
#pragma omp taskwait
for (int t = 0; t < Tn; t++)
#pragma omp task
run_shift (t, TASK_SIZE);
#pragma omp taskwait
for (int t = 0; t < Tn; t++)
#pragma omp task
run_mul (t, TASK_SIZE);
#pragma omp taskwait
for (int t = 0; t < Tn; t++)
#pragma omp task
run_div (t, TASK_SIZE);
#pragma omp taskwait
}
}
Meta-data Lookup Table for ApplicationX |  | 
Core 1 | Core 2 | ...
Task type1 | Task type 1 | 
Task type 2 | Task type 2 | 
Task type 3 | Task type 3 | 
Task type 4 | Task type 4 | 
Core 0
L1 I$
…
Core 15
L1 I$
NI
Low-latency Interconnect
BANK 1
BANK 2
BANK 32
…
DMA
Shared memory cluster
L1 DATA mem (TCDM)
…
Stage 1
Stage 2
Stage 7
Core
EDAC
ΣIR
ΣI
Meta-data
+
TEC (taski, corej) =
#I (taski, corej) + #RI (taski, corej)

## Slide 10: Centralized Variability- and Load-Aware Scheduler (CVLS)
For a taski, CVLS assigns a corej s.t. TEC (taski, corej) + loadj is minimum across the cluster
CVLS is a centralized and executed by one master thread

## Slide 11: Limitations of Centralized Queue
CVLS with single master thread consumes more cycles to find a suitable core for task assignment compared to RRS
Solution: reduce overheads via distributed task queues (private task queue for each core)
15% slower

## Slide 12: Distributed Variability- and Load-Aware Scheduler (DVLS)
DVLS shares the computational load of CVLS from one master to multiple slave threads
Master thread simply pushes tasks in a decoupled queue
Slave threads pick up a task from decoupled queue and push to best-fitted distributed queue

## Slide 13: Benefits of Decupling and Distributed Queues
This “decoupling” between queues:
Master thread proceeds fast to push tasks
The rest of threads cooperatively will schedule tasks among themselves  full utilization
44% faster
4%
faster

## Slide 14: Experimental Setup
Each core optimized during P&R with a target frequency of 850MHz.
@ Sign-off: die-to-die and within-die process variations are injected using PrimeTime VX and variation-aware 45nm TSMC libs (derived from PCA)
We integrated ILV models into SystemC-based virtual platform
Eight computational-intensive kernels accelerated by OpenMP
Core 0
L1 I$
…
Core 15
L1 I$
NI
Low-latency Interconnect
BANK 1
BANK 2
BANK 32
…
DMA
L1 DATA mem (TCDM)
C0 847 | C4 847 | C8 909 | C12 901
C1 893 | C5 909 | C9 855 | C13 820
C2 847 | C6 877 | C10 826 | C14 826
C3 901 | C7 870 | C11 917 | C15 862
Process Variation
Six cores (C0, C2, C4, C10, C13, C14) cannot meet the design time target frequency of 850 MHz

## Slide 15: Execution Time and Energy Saving
DVLS upto 47% (33% on average) faster execution than RRS
CVLS upto 29% (4% on average) faster execution than RRS
DVLS upto 44% (30% on average) energy saving compared to RRS
CVLS upto 38% (17% on average) energy saving compared to RRS

## Slide 16: Summary
Our OpenMP reduces cost of error correction in software (proper task-to-core assignment in presence of errors)
Introspective task monitoring to characterize online meta-data
Capturing both hardware variability and workload
Centralized/Distributed dispatching
Decoupling and distributed tasking queues
All threads cooperatively will schedule tasks among themselves
Distributed scheduling achieves on average 30% energy saving, and 33% performance improvement compared to RRS.