## Slide 1: Hierarchically Focused Guardbanding: An Adaptive Approach to Mitigate PVT Variations and Aging
Abbas Rahimi, Luca Benini, Rajesh K. Gupta
UC San Diego and Università di Bologna

## Slide 2: Outline
Device Variability
  Process, voltage, and temperature, and aging
Resilient Techniques
Hierarchically Focused Guardbanding
  Analysis Flow for Timing Error Rate
  Parametric Model Fitting
Hierarchical Sensors Observability
Online Utilization of HFG
  Throughput improvement
Conclusion

## Slide 3: Ever-increasing PVTA Variations
Variability in transistor characteristics is a major challenge in nanoscale CMOS, PVTA
  Static Process variation: effective transistor channel length and threshold voltage
  Dynamic variations: Temperature fluctuations, supply Voltage droops, and device Aging (NBTI, HCI)
To handle variations designers use conservative guardbands  loss of operational efficiency 
Temperature
Clock
actual circuit delay
guardband
Aging
VCC Droop
Across-wafer Frequency

## Slide 4: Resilient Techniques
Sense & Adapt
Observation using in situ monitors (Razor, EDS) with cycle-by-cycle corrections (leveraging CMOS knobs or replay)
Sense (detect)
Adapt (correct)
Sensors
Model
Prevent
Predict & Prevent
Relying on external or replica monitors Model-based rule  derive adaptive guardband to prevent error

## Slide 5: Our Resilient View
[ILV] A. Rahimi, L. Benini, R. K. Gupta, “Analysis of Instruction-level Vulnerability to Dynamic Voltage and Temperature Variations,” DATE, 2012.
[SLV] A. Rahimi, L. Benini, R. K. Gupta, “Application-Adaptive Guardbanding to Mitigate Static and Dynamic Variability,” IEEE Tran. on Computer, 2013.
[PLV] A. Rahimi, L. Benini, R. K. Gupta, “Procedure Hopping: a Low Overhead Solution to Mitigate Variability in Shared-L1 Processor Clusters,” ISLPED, 2012.
[TLV] A. Rahimi, A. Marongiu, P. Burgio, R. K. Gupta, L. Benini, “Variation-Tolerant OpenMP Tasking on Tightly-Coupled Processor Clusters,” DATE, 2013.
Sense & Adapt
We have done cross-layer vulnerability analysis: Manifestation of variability from instruction-level to task-level
Model & Prevent
In this work, we present Hierarchically Focused Guardbanding (HFG), a model-based rule to derive guardband adaptively, for avoiding PVTA-induced timing error.

## Slide 6: Contributions
A new high-level model for Timing Error Rate of various integer as well as floating-point functional units (FUs) in presence of PVTA variations.
  Online: a model-based rule to derive guardband from the PVTA sensor readings
  Offline: identifying vulnerable FUs
Notion of Hierarchically “Focused” Guardbanding (HFG) which is guided by online utilization of the model in view of monitors, observation granularity, and reaction times.
Applying HFG on GPU at two distinct granularities:
  Fine-grained granularity of instruction-by-instruction monitoring and adaptive guardbanding
  Coarse-grained granularity of kernel-level monitoring and adaptive guardbanding

## Slide 7: HFG Analysis Flow for TER
The model takes into account
  PVTA parameter variations
  Clock frequency
  Physical details of Placed-and-Routed FUs in 45nm TSMC technology
Analyzed FUs:
  10 32-bit integer
  15 single precision floating-point (fully compatible with the IEEE 754 standard)
A full permutation of PVTA parameters and clock frequency are applied.
For each FUi working with tclk and a given PVTA variations, we defined Timing Error Rate (TER):
 | Start Point | End Point | Step | # of Points
Voltage | 0.88V | 1.10V | 0.01V | 23
Temperature | 0°C | 120°C | 10°C | 13
Process (σWID) | 0% | 9.6% | 3.2% | 4
Aging (∆Vth) | 0mV | 100mV | 25mV | 5
tclk | 0.2ns | 5.0ns | 0.2ns | 25
Notes: CriticalPaths are those paths with a negative slack that cannot meet the setup-time of flip-flops with the clock period of tclk under certain PVTA variations, and Σ Paths is the total number of paths in FUi. After the back-end optimizations, dur-ing the sign-off, we calculate TER by analysis of FU PVTA parameter variations

## Slide 8: Parametric Model Fitting
We used Supervised learning (linear discriminant analysis) to generate a parametric model at the level of FU that relates PVTA parameters variation and tclk to classes of TER.
On average, for all FUs the resubstitution error is 0.036, meaning the models classify nearly all data correctly.
For extra characterization points, the model makes correct estimates for 97% of out-of-sample data. The remaining 3% is misclassified to the high-error rate class, CH, thus will have safe guardband.
HFG ASIC Analysis Flow for TER
PVTA
tclk
TER=0% | 33%>= TER >0% | 66%>= TER >33% | 100%>= TER >66%
Class0 (C0) | ClassLow (CL) | ClassMedium (CM) | ClassHigh (CH)
Classes of TER
TER
TER
Class
Linear discriminant analysis
Parametric Model

## Slide 9: Delay Variation and TER Characterization
During design time the delay of the FP adder has a large uncertainty of [0.73ns,1.32ns], since the actual values of PVTA parameters are unknown.

## Slide 10: Hierarchical Sensors Observability
The question is that mix of monitors that would be useful?
The more sensors we provide for a FU, the better conservative guardband reduction for that FU.
The guardband of FP adder can be reduced up to
  8% (P_sensor),
  24% (PA_sensors),
  28% (PAT_sensors),
  44% (PATV_sensors)
Sensor overheads:
  In-situ PVT sensors impose 1−3% area overhead [Bowman’09]
  Five replica PVT sensors increase area of by 0.2% [Lefurgy’11]
  The banks of 96 NBTI aging sensors occupy less than 0.01% of the core's area [Singh’11]

## Slide 11: Online Utilization of HFG
The control system tunes the clock frequency through an online model-based rule.
To support fast controller's computation, the parametric model generates distinct Look Up Tables (LUTs) for every FUs
We apply HFG to architecture at two granularities
  Fine-grained granularity of instruction-by-instruction monitoring and adaptation that signals of PATV sensors come from individual FUs
  Coarse-grained granularity of kernel-level monitoring uses a representative PATV sensors for the entire execution stage of pipeline
Notes: Since TER characterization considers the static critical paths (which might not be activated during execution of certain dynamic inputs), the model always returns an upper bound of the actual TER, thus returned tclk of LUTs guarantees the target TER.

## Slide 12: Throughput benefit of HFG
At kernel-level monitoring, on average, the throughput increases by 70%, when the PE moves from only P_sensor to PATV_sensors scenario. The target TER is set to “0” in preference to the error-intolerant applications.
Instruction-by-instruction monitoring and adaptation improves the throughput by 1.8×−2.1× depends to the PATV sensors configuration and kernel's instructions.

## Slide 13: Conclusion
We present a model ‡ and its usage for online variation-aware resource management as well as design time analysis of vulnerable functional units through an accurate 45nm TSMC flow.
The model is used as an adaptive resource management technique to proactively prevent timing error by applying a focused guardbanding.
We demonstrate the effectiveness of HFG on GPU architecture at two granularities of observation and adaptation: (i) fine-grained instruction-level; and (ii) coarse-grained kernel-level.
‡publicly available for download at: http://mesl.ucsd.edu/site/PVTA_MODELS/models.htm

## Slide 14
Thank You!
NSF Variability Expedition
ERC MultiTherman