## Slide 1: Variation-Tolerant OpenMP Tasking on Tightly-Coupled Processor Clusters
A. Rahimi, A. Marongiu, P. Burgio, R. K. Gupta, L. Benini
UC San Diego and Università di Bologna

## Slide 2: Outline
Device Variability
  Process, voltage, and temperature variations
Why OpenMP and why tasking?
Task-Level Vulnerability (TLV)
Variation-Tolerant Architecture
Inter- and Intra-corner TLV
Variation-Tolerant OpenMP Tasking
  Variation-Aware Reactive Scheduling Algorithm
Experimental Reults

## Slide 3: Ever-increasing Proc.-Vol.-Tem. Variations
Variability in transistor characteristics is a major challenge in nanoscale CMOS
  Static Process variation, e.g., 40% VTH
  Dynamic variations, e.g., 160˚∆C temperature fluctuations and 10% supply voltage droops.
To handle variations designers use conservative guardbands  loss of operational efficiency 

## Slide 4: Approaches to Variability-Tolerance
Design time conservative guardbanding
Post silicon binning
Runtime tolerance by various adaptiveness, e.g., replay errant instructions
This approach
relies on online measurements of errors
creates runtime overhead for both [Bowman’11]
  Latency (up to 28 extra recovery cycles per error)
  Energy overhead of 26nJ
that should be minimized

## Slide 5: Why a Variation-Aware OpenMP?
Variations are more exacerbated by many-core systems:
  Multiple voltage-temperature islands
  Cores in various islands display different error rate
The programming model and runtime environment of MIMD should be aware of variations.
847 MHz | 847MHz | 909MHz | 901MHz
893MHz | 909MHz | 855MHz | 820MHz
847MHz | 877MHz | 826MHz | 826MHz
901MHz | 870 MHz | 917MHz | 862MHz
Frequency variation of a 16-core cluster due to WID and D2D process variation
Core0 at 1.1V faces 7.3K errant instructions 
Core1 at 0.81V faces 428K errant instructions 

## Slide 6: Why OpenMP Tasking?
Sequence-level Vulnerability (SLV)
Instruction-level Vulnerability (ILV)
Procedure-level Vulnerability (PLV)
Task-level Vulnerability (TLV)
[ILV] A. Rahimi, L. Benini, R. K. Gupta, “Analysis of Instruction-level Vulnerability to Dynamic Voltage and Temperature Variations,” DATE, 2012.
[SLV] A. Rahimi, L. Benini, R. K. Gupta, “Application-Adaptive Guardbanding to Mitigate Static and Dynamic Variability,” IEEE Tran. on Computer, 2013 (to appear)
[PLV] A. Rahimi, L. Benini, R. K. Gupta, “Procedure Hopping: a Low Overhead Solution to Mitigate Variability in Shared-L1 Processor Clusters,” ISLPED, 2012.
The steps to build variability abstractions up to the SW layer
Task-Level Vulnerability (TLV) as metadata to characterize variations.
TLV is a vertical abstraction: TLV reflects manifestation of circuit-level variability in specific parallel software context.
The right granularity:
  To observe and react for OMP scheduler
  A convenient abstraction for programmers to express irregular and unstructured parallelism.

## Slide 7: Instruction-Level Vulnerability (ILV)*
The ILV for each instructioni at every operating condition is quantified:
  where Ni is the total number of clock cycles in Monte Carlo simulation of instructioni with random operands.
  Violationj indicates whether there is a violated stage at clock cyclej or not.
ILVi defines as the total number of violated cycles over the total simulated cycles for the instructioni.
Therefore, the lower ILV, the better
*A. Rahimi, L. Benini, R. K. Gupta, “Analysis of Instruction-level Vulnerability to Dynamic Voltage and Temperature Variations,” DATE, 2012.

## Slide 8: Task-Level Vulnerability (TLV)
ILV represents a useful variability metric that raises the level of abstraction from the circuit (critical paths) to the ISA-level.
ILV is extended to a more coarse-grained task-level metric, TLV, towards building an integrated, vertical approach to control variability.
TLV is a per core and per task type metric:
  ∑EI is # of errant instructions during taskj on corei
  Length is total # of executed instructions
The lower TLV, the better 

## Slide 9: Variation-Tolerant MP Cluster (1/2)
Inspired by STM STHORM
16x 32-bit RISC cores
L1 SW-managed Tightly Coupled Data Memory (TCDM)
Multi-banked/multi-ported
Fast concurrent read access
Fast Log. Interconnect
One clock domain
Bridge towards NoC
SHARED L1 TCDM
BANK 0
SLAVE
PORT
LOW-LATENCY LOGARITHMIC INTERCONNECT
BANK 1
SLAVE
PORT
BANK N
SLAVE
PORT
test-and-set semaphores
SLAVE
PORT
L2/L3
BRIDGE
CORE 0
MASTER
PORT
I$
Var. sensor
VDD-hopping
Replay
I$
CORE M
Var. sensor
VDD-hopping
Replay
I$
MASTER
PORT
VDD-Hopping
Replay
Var-Sensor
I$
CORE 0
MASTER PORT

## Slide 10: Variation-Tolerant Architecture (2/2)
Every core is equipped with:
  Error sensing (EDS [Bowman’09])
    detect any timing error due to dynamic delay variation
  Error recovery (Multiple-issue replay mechanism [Bowman’11])
    to recover the errant instruction without changing the clock frequency
  VDD hopping (semi-static) [Miermont’07]
    to compensate the impact of static process variation [Rahimi’12]
Thus, cluster enables per-core characterization of TLV metadata
VDD-Hopping
Replay
Var-Sensor
I$
CORE 0
MASTER PORT
Online variability measurement  TLV metadata characterization
Fast access to the TLV metadata for each type of task is guaranteed by carefully placing these key data structures in L1 TCDM.

## Slide 11: OpenMP Tasking
TCDM
Task descriptors created upon encountering a task directive
Task fetched by any core encountering a barrier
task directives identify given portions of code (tasks)
A task type is defined for every occurrence of the task directive in the program
#pragma omp parallel
{
#pragma omp single
{
for (i = 1...N) {
#pragma omp task
FUNC_1 (i);
#pragma omp task
FUNC_2 (i);
}
}
} /* implicit barrier */
Task queue
Push task
Fetch and execute (FIFO)
Task descriptor
two task types

## Slide 12: Intra- and Inter-Corner TLV
TLV across various type of tasks: TLV of each type of tasks is different (up to 9×) even within the fixed operating condition in a corei
Inter-corner TLV
Intra-corner TLV at fix (25°C, 1.1V)
Inter-corner TLV (across various operating conditions for 45nm)
  The average TLV of the six types of tasks is an increasing function of temperature.
  In contrast, decreasing the voltage from the nominal point of 1.1V increases TLV.

## Slide 13: Variation-tolerant OpenMP Tasking
TCDM
task types
cores
Online TLV characterization
  TLV table: LUT containing TLV for every core and task type
  Reside in TCDM. Parallel inspection from multiple cores
Each core collects TLV information in parallel
  Distributed scheduler
  LUT updated at every task execution
void handle_tasks () {
while (HAVE_TASKS) { // Task scheduling loop
task_desc_t *t = EXTRACT_TASK ();
if (t) {
float Otlv = tlv_read_task_metadata (core_id);
/* Reset counter for this core */
tlv_reset_task_metadata (core_id);
/* EXEC! */
t->task_fn (t->task_data);
/* We executed. Fetch TLV ...*/
float tlv = tlv_read_task_metadata (core_id);
/* Update TLV. Average new and old value */
tlv_table_write(t->task_type_id, core_id, (tlv-Otlv)/2);
}
}
}
 | C0 | C1 | C2
T0 | 0.0211 |  | -
T1 | 0.891 | - | 0.000005
VDD-Hopping
Replay
Var-Sensor
I$
CORE 0
MASTER PORT
0.11
TLV-table

## Slide 14: TLV-aware Extensions
#pragma omp parallel
{
#pragma omp single
{
for (i = 1...N) {
#pragma omp task
FUNC_1 (i);
#pragma omp task
FUNC_2 (i);
}
}
} /* implicit barrier */
TCDM
Variation-tolerant OpenMP scheduler
  Reactive scheduling. Idle processors trying to fetch a task check if their TLV for the task is under a certain threshold to minimize number of errant instructions (and costly replay cycles)
  limited number of rejects for a given tasks, to avoid starvation
Task queue
Fetch and execute (FIFO)
TLV-aware fetch
Task descriptor

## Slide 15: Variation-aware Scheduling Algorithm
TCDM
taskj = PEEK_QUEUE()
TLV(i,j) = tlv_table_read(corei, taskj);
if (TLV(i,j)> TLV_THR && corei_escape_cnt <ESCAPE_THR)
{
corei_escape_cnt ++;
escape (taskj);
}
else
{
assign_to_corei (taskj);
corei_escape_cnt = 0;
}
 | C0 | C1 | C2
T0 | 0.0211 | 0.11 | -
T1 | 0.891 | - | 0.000005
C0 | C1 | C2
1 | 5 | 0
TLV-table
core_escape_cnt
Task queue

## Slide 16: Experimental Setup: Arch. + Benchmarks
Architecture: SystemC-based virtual platform* modeling the tightly-coupled cluster
Benchmark: Seven widely used computational kernels from the image processing domain are parallelized using OpenMP tasking. On average 375 dynamic tasks.
The TLV lookup table only occupies 104−448 Bytes depending upon the number of task types.
*D. Bortolotti et al., “Exploring instruction caching strategies for tightly-coupled shared-memory clusters,” Proc. Intern.Symposium on System on Chip (SoC), pp.34-41, 2011
ARM v6 core | 16 | TCDM banks | 16
I$ size | 16KB per core | TCDM latency | 2 cycles
I$ line | 4 words | TCDM size | 256 KB
Latency hit | 1 cycle | L3 latency | ≥ 60 cycles
Latency miss | ≥ 59 cycles | L3 size | 256MB

## Slide 17: Experimental Setup: Variability Modeling
To emulate variations, we have integrated variations models at the level of individual instructions using the ILV characterization methodology.
ILV models of 16-core LEON-3 for TSMC 45-nm, general-purpose process with normal VTH cells.
Vdd-hopping is applied to compensate injected process variation.
C0 >850 | C4 >850 | C8 909 | C12 901
C1 893 | C5 909 | C9 855 | C13 >850
C2 >850 | C6 877 | C10 >850 | C14 >850
C3 901 | C7 870 | C11 917 | C15 862
VDD={ | 1.1V, | 0.97V, | 0.81V | }
C0 847 | C4 847 | C8 909 | C12 901
C1 893 | C5 909 | C9 855 | C13 820
C2 847 | C6 877 | C10 826 | C14 826
C3 901 | C7 870 | C11 917 | C15 862
Each core optimized during P&R with a target frequency of 850MHz.
@ Sign-off: die-to-die and within-die process variations are injected using PrimeTime VX and variation-aware 45nm TSMC libs (derived from PCA)
Six cores (C0, C2, C4, C10, C13, C14) cannot meet the design time target frequency of 850 MHz 
All cores can work with the design time target frequency of 850 MHz  but multiple voltage OpPs 
Process Variation
Vdd-Hopping

## Slide 18: Overhead of Variation-tolerant Scheduler
Normalized IPC = IPC variation-aware scheduler / IPC OMP baseline scheduler
On a variation-immune cluster, on average, the normalized IPC of the cluster is slightly decreased by 0.998×. Due to
  reading the TLV lookup table
  checking the conditions

## Slide 19: IPC of Variability-affected Cluster
Our scheduler decreases the number of cycles per cluster for each type of tasks, because cores incur fewer errant instructions and spend lower cycles for recovery.
The normalized IPC is increased by 1.17× (on average) for all benchmarks executing at 10°C. At temperature of 100°C (ΔT=90°C) IPC is increased by 1.15 ×.
M= Number of times that the scheduler postponing the execution of the task in the head of queue.
On average, each task is escaped 2.1 times.

## Slide 20: Conclusion
Vertical abstraction of circuit-level variations into a high-level parallel software execution (OpenMP 3.0 tasking)
The vulnerability of tasks is characterized by TLV metadata during introspective execution
The reactive variation-tolerant runtime scheduler utilizes TLV to match cores with tasks
The normalized IPC of 16-core variability-affected cluster increases up to 1.51× (on average, 1.15×).
Future work: multiple clusters @ multiple dynamic OpP in Vdd & f

## Slide 21
Grazie dell’attenzione!
NSF Variability Expedition
ERC MultiTherman

## Slide 22: Classification of Instructions Based ILV
Instructions are partitioned into three main classes:
  1st Class: Logical & arithmetic instructions
  2nd Class: Memory instructions
  3rd Class: Hardware multiply & divide instructions
For every operating conditions:
ILV (3rd Class) ≥ ILV (2nd Class) ≥ ILV (1st Class)
(V, T) |  | (0.88V, -40°C) |  |  |  |  |  | (0.88V, 0°C) |  |  |  |  | (0.88V, 125°C) |  |  |  |  | 
Cycle time (ns) |  | 1 | 1.02 | 1.06 | 1.08 | 1.10 | 1.12 | 1 | 1.02 | 1.06 | 1.10 | 1.12 | 1.04 | 1.06 | 1.08 | 1.10 | 1.16 | 1.18
Logical & Arithmetic | add | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
 | and | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
 | or | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
 | sll | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
 | sra | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
 | srl | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
 | sub | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
 | xnor | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
 | xor | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
Mem | load | 1 | 0.824 | 0 | 0 | 0 | 0 | 1 | 0.707 | 0 | 0 | 0 | 1 | 0.796 | 0 | 0 | 0 | 0
 | store | 1 | 0.847 | 0 | 0 | 0 | 0 | 1 | 0.743 | 0 | 0 | 0 | 1 | 0.823 | 0 | 0 | 0 | 0
Mul.&Div | mul | 1 | 0.996 | 0.064 | 0.027 | 0.017 | 0 | 1 | 0.996 | 0.065 | 0.018 | 0 | 1 | 0.876 | 0.876 | 0.016 | 06 | 0
 | div | 1 | 0.991 | 0.989 | 0.989 | 0.984 | 0 | 1 | 0.994 | 0.991 | 0.973 | 0 | 1 | 0.991 | 0.991 | 0.991 | 0.984 | 0
ILV at 0.88V, while varying temperature for 65nm: