## Slide 1: Temporal Memoization for Energy-Efficient Timing Error Recovery in GPGPUs
Abbas Rahimi, Luca Benini, Rajesh K. Gupta
UC San Diego, UNIBO and ETHZ
NSF Variability Expedition
ERC MultiTherman

## Slide 2: Outline
Motivation
  Sources of variability
  Cost of variability-tolerance
Related work
  Taxonomy of SIMD Variability-Tolerance
Temporal memoization
Temporal instruction reuse in GPGPUs
Experimental setup and results
Conclusions and future work

## Slide 3: Sources of Variability
Variability in transistor characteristics is a major challenge in nanoscale CMOS:
  Static variation: process (Leff, Vth)
  Dynamic variations: aging, temperature, voltage droops
To handle variations
  Conservative guardbands  loss of operational efficiency 
actual circuit delay
Process
Temperature
Aging
VCC droop
Clock
guardband
Slow
Fast

## Slide 4: Variability is about Cost and Scale
3
Eliminating guardband 
Timing error 
Costly error recovery 
3×N recovery cycles per error for scalar pipeline!
N= # of stages
Bowman et al, JSSC’09
Bowman et al, JSSC’11

## Slide 5: Cost of Recovery is Higher in SIMD!
Cost of recovery is exacerbated in SIMD pipelined:
  Vertically: Any error within any of the lanes will cause a global stall and recovery of the entire SIMD pipeline.
  Horizontally: Higher pipeline latency causes a higher cost of recovery through flushing and replaying.
quadratically expensive
Wide lanes
Deep pipes
error rate × wider width
Recovery cycles increases linearly with pipeline length

## Slide 6: SIMD is the Heart of GPGPU
Radeon HD 5870 (AMD Evergreen)
  20 Compute Units (CUs)
    16 Stream Cores (SCs) per CU (SIMD execution)
      5 Processing Elements (PEs) per SC (VLIW execution)
        4 Identical PEs (PEX, PEY, PEW, PEZ)
        1 Special PET
Ultra-threaded Dispatcher
Compute Unit (CU0)
Compute Unit (CU19)
L1
L1
Crossbar
Global Memory Hierarchy
Compute Device
SIMD Fetch Unit
Stream Core (SC0)
Stream Core (SC15)
Local Data Storage
Wavefront Scheduler
Compute Unit (CU)
T
General-purpose Reg
X
Y
Z
W
Branch
Processing Elements (PEs)
Stream Core (SC)
X : MOV R8.x, 0.0f
Y : AND_INT T0.y, KC0[1].x
Z : ASHR T0.x, KC1[3].x
W:________
T:_________
VLIW

## Slide 7: Taxonomy of SIMD Variability-Tolerance
6
Guardband
Timing error
Error recovery
Decoupled recovery
Memoization
Lane decoupling through provate queues
Recalling recent context of error-free execution
No timing error
Eliminating
Adaptive
Detect-then-correct
Predict & prevent
Hierarchically focused guardbanding and uniform instruction assignment
Pawlowski et al, ISSCC’12
Krimer et al, ISCA’12
Rahimi et al, TCAS’13
Rahimi et al, DATE’13
Rahimi et al, DAC’13

## Slide 8: Related Work: Predict & Prevent
Uniform VLIW assignment periodically distributes the stress of instructions among various slots resulting in a healthy code generation.
GPGPU
Dynamic Binary Optimizer
Host CPU
Naïve Kernel
Healthy Kernel
Rahimi et al, DAC’13
Tuning clock frequency through an online model-based rule in view of sensors, observation granularity, and reaction times.
Rahimi et al, DATE’13
× These predictive techniques cannot eliminate the entire guardbanding to work efficiently at the edge of failure!

## Slide 9: Related Work: Detect-then-Correct
Lane decoupling by private queues that prevent errors in any single lane from stalling all other lanes self-lane recovery
Pawlowski et al, ISSCC’12
Krimer et al, ISCA’12
  Causes slip between lanes  additional mechanisms to ensure correct execution
  Lanes are required to resynchronize for a microbarrier (load, store)  performance penalty

## Slide 10: Taxonomy of SIMD Variability-Tolerance
9
Guardband
Timing error
Error ignorance
Error recovery
Decoupled recovery
Memoization
Lane decoupling through provate queues
Recalling recent context of error-free execution
Ensuring safety of error ignorance by fusing multiple data-parallel values into a single value
No timing error
Eliminating
Adaptive
Detect-then-correct
Detect & ignore
Predict & prevent
Hierarchically focused guardbanding and uniform instruction assignment
Detect-then-correct:
exactly or approximately through memoization

## Slide 11: Memoization: in Time or Space
Reduce the cost of recovery by memoization-based optimizations that exploit spatial or temporal parallelisms
Sensors
HW
Contexta [t]
✔
Contexti
x
Reuse
Contexta [t-1]
✔
Contexta [t-k]
✔
…
Contextb [t]
✔
Contextb [t-1]
✔
Contextb [t-k]
✔
…
Contextc [t]
✔
Contextc [t-1]
✔
Contextc [t-k]
✔
…
Spatial error correction
Temporal error correction
[Spatial Memoization] A. Rahimi, L. Benini, R. K. Gupta, “Spatial Memoization: Concurrent Instruction Reuse to Correct Timing Errors in SIMD,” IEEE Tran. on CAS-II, 2013.

## Slide 12: Contributions
A temporal memoization technique for use in SIMD floating-point units (FPUs) in GPGPUs
  Recalls the context of error-free execution of an instruction on a FPU.
  Maintain the lock-step execution 
To enable scalable and independent recovery, a single-cycle lookup table (LUT) is tightly coupled to every FPU to maintain contexts of recent error-free executions.
The LUT reuses these memorized contexts to exactly, or approximately, correct errant FP instructions based on application needs.
Scalability ✓
low-cost self-resiliency ✓
in the face of high timing error rates!

## Slide 13: Concurrent/Temporal Inst. Reuse (C/TIR)
Parallel execution in SIMD provides an ability to reuse computation and reduce the cost of recovery by leveraging inherent value locality
  CIR: Whether an instruction can be reused spatially across various parallel lanes?
  TIR: Whether an instruction can be reused temporally for a lane itself?
Utilizing memoization:
    C/TIR memoizes the result of an error-free execution on an instance of data.
    Reuses this memoized context if they meet a matching constraint (approximate or exact)
Concurrent/Temporal Inst. Reuse (C/TIR)
12
CIR
TIR

## Slide 14: FP Temporal Instruction Reuse (TIR)
11%↑
13%↑
5×↑
A private FIFO for every individual FPU
  Exact matching constraint; for Black-Scholes
  Approximate matching constraint (ignoring the less significant 12 bits of the fraction); for Sobel
With approximate matching constraint, PSNR > 30dB✓

## Slide 15: Overall TIR Rate of Applications
Mostly, hit rate increases < 10% when FIFO increases from 10 to 1,000
FIFOs with 4 entries
  ✓ provide an average hit rate of 76% (up to 97%)
  ✓ have 2.8× higher hit rate per power compared to the 10 entries
Approximate matching
Exact matching
Programmable through
memory-mapped registers

## Slide 16: Temporal Memoization Module
temporal memoization
module (in gray) superposed on the baseline recovery with EDS+ECU (replay)
Hit | Error | Action | QPipe
0 | 0 | LUT update | QS
0 | 1 | Trigger ECU | QS
1 | 0 | LUT reuse + FP CLK gating | QL
1 | 1 | LUT reuse + FP CLK gating + error masking | QL

## Slide 17: Experimental Setup
We focus on energy-hungry high-latency single-precision FP pipelines
  Memory blocks are resilient by using tunable replica bits
  The fetch and decode stages display a low criticality [Rahimi et al, DATE’12]
  Six frequently exercised units: ADD, MUL, SQRT, RECIP, MULADD, FP2FIX; 4 cycles latency (except RECIP with 16 stages) generated by FloPoCo.
Have been optimized for signoff frequency of 1GHz at (SS/0.81V/125°C), and then for power using high VTH cells in TSMC 45nm. 0.11% die area overhead for Radeon HD 5870.
Multi2Sim, a cycle-accurate CPU-GPU simulator for AMD Evergreen
The naive binaries of AMD APP SDK 2.5

## Slide 18: Energy Saving for Various Error Rates
error rate of 0%: on average 8% saving
error rate of 1%: on average 14% saving
error rate of 2%: on average 20% saving
error rate of 3%: on average 24% saving
error rate of 4%: on average 28% saving
Temporal memoization module does NOT produce an erroneous result, as it has a positive slack of 14% of the clock period.
Thanks to efficient memoization-based error recovery that does not impose any latency penalty as opposed to the baseline

## Slide 19: Efficiency under Voltage Overscaling
8% saving @ nominal volt
6% saving
66% saving
FPUs of the baseline are reduced their power as consequence of negligible error rate, while we cannot proportionally scale down the power of the temporal memoization modules.
Baseline faces an abrupt increasing in error rate therefore frequent recoveries!

## Slide 20: Conclusion
A fast lightweight temporal memoization module to independently store recent error-free executions of a FPU.
To efficiently reuse computations, the technique supports both exact and approximate error correction.
Reduces the total energy by average savings of 8%-28% depending on the timing error rate.
Enhances robustness in the voltage overscaling regime and achieves relative average energy saving of 66% with 11% voltage overscaling.

## Slide 21: Work in Progress
To further reduce the cost of memoization, we replaced LUT with associative memristive (ReRAM) memory module that has a ternary content addressable memory [Rahimi et al, DAC’14]
  39% reduction in average energy use by the kernels
Collaborative compilation + Approximate storage

## Slide 22
Grazie dell’attenzione!
NSF Variability Expedition
ERC MultiTherman