## Slide 1
Approximate Associative Memristive Memory for Energy-Efficient GPUs
Abbas Rahimi, Amirali Ghofrani, Kwang-Ting Cheng, Luca Benini, Rajesh K. Gupta
UC San Diego, UC Santa Barbara, ETH Zurich
NSF Variability Expedition
ERC MultiTherman

## Slide 2: Outline
Motivation
  Energy Efficiency in GPUs
Approximate Associative Memristive Memory
  Memoization using memristor under VOS
  Programming flow
TCAM Operation
  Approximate TCAM operation
Experimental Setup and Results
Conclusion

## Slide 3: Why GPU?
CPU
Westmere 32nm
1690 pJ/flop
GPU
Kepler 28nm
140 pJ/flop

## Slide 4: Why GPU?

## Slide 5: AMD GPU Architecture
4
Radeon HD 7970 device from Southern Islands family
  32 compute units
    4 SIMD units
      16 stream cores (parallel lanes)
2048 stream cores per device
Thermal design power: 300W!
Local Memory
Wavefront Scheduler
Compute Unit
SIMD Unit 1
SIMD Unit 2
SIMD Unit 3
SIMD Unit 4
Ultra-threaded Dispatcher
Compute Unit 1
Compute Unit 32
Global Memory
Compute Device
…
IF/ID
Vector/Scalar RF
SIMD Unit
Stream Core 16
Stream Core 1
Stream Core 2
Stream Core 3
…

## Slide 6: Voltage Over-Scaling (VOS)
VOS achieves energy efficiency at costs to:
  Performance loss
   SIMD 
  Increasing timing sensitivity in the presence of variations
   Timing errors 
5X
Dreslinski et al, Proc. IEEEE’10

## Slide 7: Timing Errors Kill SIMD!
Cost of error recovery is exacerbated in SIMD pipelined:
  Horizontally: higher pipeline latency  higher cost of recovery through flushing and replaying
  Vertically: any error within any of the lanes  global stall  recovery of the entire SIMD
6
Deep pipeline
SIMD Unit
IF/ID
….
RF
ALU
M
WB
RF
ALU
M
WB
RF
ALU
M
WB
Wide lanes
More expensive recovery

## Slide 8: SIMD Error-Tolerance
Timing error
Error handling
Independent lane
Memoization
Lane decoupling through private queues
Recalling recent context of error-free execution
No timing error
Eliminating
Adaptive
Hierarchically focused guardbanding and adaptive instruction assignment
Pawlowski et al, ISSCC’12
Krimer et al, ISCA’12
Rahimi et al, TCAS’13
Rahimi et al, DATE’14
Rahimi et al, DATE’13
Rahimi et al, DAC’13
Accepting errors
Error recovery
Guardband

## Slide 9: Our Contributions
Energy saving for GPUs, subject to few controllable timing errors
Combining Memoization + VOS
Designing Approximate Associative Memristive Memory (A2M2)
  Accepts 0-2 Hamming distance matches

## Slide 10: Why Memristor?
Memristor is a 2 terminal resistive memory
Offers high density and low energy operation with 1.0V–270mV
Downside is limited durability beyond billion write operations
30x denser!
SRAM: 120 F2
Memristor: 4F2

## Slide 11: Memristor Is Reality: Fabricated Chips
1-Mb memristor chip in 28nm [Chang, ISSCC’14]
404ns read access time at VDD = 0.27V
4-Mb memristor chip [Chang, JSSC’13]
7.2 ns read-write access time
Reliable operations: a process-temperature detector with feedback

## Slide 12: Approximate Associative Memristive Memory (A2M2)
A2M2 is tightly-integrated with FPU
A2M2 is composed of a TCAM + Memory
Mimics partial functionality of the related FPU
A2M2 is a software programmable module
  Profiler extracts highly frequent computations
  Pre-stores these computations in A2M2
A2M2 memorizes highly frequent computations  enables computing-with-memristor memory

## Slide 13: A2M2 Programming Flow
Host code
Profiler
√ : {e1} → {q1}
*: {c1, d1} → {p1}
+: {a1, b1} → {o1} +: {a2, b2} → {o2}
Kernel code
Highly frequent computations (HFC)
…
A2M2
+ FPU
A2M2
* FPU
A2M2
√ FPU
A2M2
Stream core
GPU device
Design time
Runtime
HFC +
Exact/1HD/2HDAppr
Functional Sim
√ : 2HD Appr
*: 1HD Appr
+: 1HD Appr
…: Exact
Desired PSNR

## Slide 14: Computing with A2M2
Execution stage of FPU
Ternary content addressable memory (TCAM)
2T-2R (2-transistor/2-resistive)
2-bit encoding
Stores high-frequent input patterns
Search operands
Return pre-stored result
Operands
Result
Hit
Approximate
…
A2M2
+ FPU
A2M2
* FPU
A2M2
√ FPU
A2M2
Stream core

## Slide 15: Outline
Motivation
  Energy Efficiency in GPUs
Approximate Associative Memristive Memory
  Memoization using memristor under VOS
  Programming flow
TCAM Operation
  Approximate TCAM operation
Experimental Setup and Results
Conclusion

## Slide 16: TCAM Operation
Each bit is represented by a 2T-2R cell
A match line (ML) is pre-charged to VDD
Search pattern is applied on select transistors
Stored pattern is available on memristors
Mismatched patterns result in a low-resistance path to GND and discharge ML
Search Pattern | SL | SL_b
0 | 0 | 1
1 | 1 | 0
X | 0 | 0
1
0
0
1
1
0
Search for 101: match – no discharge
1
0
1
0
1
0
Search for 110: mismatch –discharge
Stored pattern= 10X

## Slide 17: Approximate TCAM Operation
Faster reads or lower supply voltages subject to controllable approximate matching
  1000mv: Exact Matching
  775mv: 1-HD Matching
  720mv: 2-HD Matching
Precharge
Evaluation
Precharge
Evaluation
Precharge
Evaluation
1000mV
775mV
725mV

## Slide 18: Outline
Motivation
  Energy Efficiency in GPUs
Approximate Associative Memristive Memory
  Memoization using memristor under VOS
  Programming flow
TCAM Operation
  Approximate TCAM operation
Experimental Setup and Results
Conclusion

## Slide 19: Experimental Setup
AMD GPUs
  Image processing applications from AMD APP SDK v2.5
  Multi2Sim for AMD Southern Islands GPU, Radeon HD 7970 device
FPU ASIC flow
  6-stage balanced FPUs generated by FloPoCo
  Synthesized and mapped using a 45-nm TSMC
  Optimized for power and a signoff clock period of 1.5ns:
    Synopsys Design Compiler/ IC Compiler
    FPU power estimation: Synopsys PrimeTime (1.0V)
A2M2 design flow
  Transistor-level SPICE simulations by Cadence Virtuoso for power and delay estimation

## Slide 20: Energy Comparison: FPU versus A2M2
Module | FPU (1.0V) | Exact |  | Approximate (2-HD) | 
 |  | 32-row | 64-row | 32-row | 64-row
ADD | 4742 | 2740 | 4568 | 999 | 1479
MUL | 9891 | 2740 | 4568 | 999 | 1479
SQRT | 9983 | 2322 | 3901 | 864 | 1332
MAC | 12051 | 3096 | 5071 | 1124 | 1627
Energy ratio | 1 | 0.34 | 0.56 | 0.12 | 0.18
Energy (fJ) per operation in 45nm

## Slide 21: Hit Rate versus Size/Accuracy
12%
18%
12%
Exact Matching
Approximate Matching (2-HD)

## Slide 22: Energy Saving: Sobel Filter
Chart: 
| 4 | 8 | 16 | 32 | 64
Energy (Exact) | 0.94275 | 0.8405 | 0.89156 | 0.99333 | 1.2029
Energy (1-HD Appr) | 0.80196 | 0.71525 | 0.73081 | 0.76346 | 0.83556
PSNR (1-HD Appr) | 54 | 45.23 | 40.45 | 37.8 | 26
24%
26%
28%
20%

## Slide 23: Energy Saving: Roberts Filter
43%
40%
44%
45%
PSNR > 30dB
A2M2 with 8-row: Sobel (28%), Sharpen (23%), and Shift (34%)
A2M2 with 16-row: Robert (45%)

## Slide 24: Visual Depiction of Output Quality
Quality loss is nearly indiscernible to the eye, whereas provides 28% energy savings

## Slide 25: Conclusion
Approximate Associative Memristive Modules combines:
  Benefits of emerging memristor technology
  Tolerance of emerging approximate computing
A2M2 tightly integrated to FPU to save energy by
  Recalling the frequent computations therefore avoiding re-executions
  Operating at VOS by accepting the approximate matches (1-HD and 2-HD)
A2M2 saves 32% energy on average with 8-row

## Slide 26
Thanks!