## Slide 1
Axilog: Language Support for Approximate Hardware Design
DATE 2015
Georgia Institute of Technology Alternative Computing Technologies (ACT) Lab
Georgia Institute of Technology University of Minnesota UC San Diego
Amir Yazdanbakhsh
Divya Mahajan
Bradley Thwaites
Jongse Park
Anandhavel Nagendrakumar
Sindhuja Sethuraman
Kartik Ramkrishnan
Nishanthi Ravindran
Rudra Jariwala
Abbas Rahimi
Hadi Esmaeilzadeh
Kia Bazargan

## Slide 2: Approximate computing Embracing error
Relax the abstraction of near-perfect accuracy in general-purpose computing/communication/storage
Allow errors to happen during computation/communication/storage
  Improve resource utilization efficiency
    Energy, bandwidth, capacity, …
  Improve performance
Build acceptable systems from intentionally-made unreliable software and hardware components
Avoid overkill and worst-case design

## Slide 3: Avoiding Worst-Case Design Approximate Computing
Generality
Precision
Reliability
Determinism
Efficiency
Performance
Cost
Cost
Physical Device
Circuit
Architecutre
Compiler
Programming Language
Application
Microarchitecture

## Slide 4
Goals
Design the first HDL for
  Approximate Hw Design
  Approximate Hw Reuse
  Approximate Synthesis
Criteria
Approximate HDL shall be
  High-level
  Automated
  Backward compatible

## Slide 5: Safety in Hardware
Controller
Datapath
Clock
Precise
Approximate
Precise

## Slide 6
Axilog Annotations
Design Annotations
relax (relax_local)
restrict (restrict_global)
Reuse Annotations
approximate
bridge
critical

## Slide 7
Design Annotations

## Slide 8: Relaxing Accuracy Requirements
module ripple_carry_adder(a, b, c_in, c_out, s)
…
full_adder f0(a[0], b[0], c_in, w0, s[0])
full_adder f1(a[1], b[1], w0, c_out, s[1])
relax (s);
…

## Slide 9: Relaxing Accuracy Requirements
module ripple_carry_adder(a, b, c_in, c_out, s)
…
full_adder f0(a[0], b[0], c_in, w0, s[0])
full_adder f1(a[1], b[1], w0, c_out, s[1])
relax (s);
…

## Slide 10: Scoping Approximation (relax_local)
module full_adder (a, b, c_in, c_out, s)
…
relax_local (s);
…
…
full_adder f0 (…)
full_adder f1(…)
relax (s[0]);
…

## Slide 11: Scoping Approximation (relax_local)
module full_adder (a, b, c_in, c_out, s)
…
relax_local (s);
…
…
full_adder f0 (…)
full_adder f1(…)
relax (s[0]);
…

## Slide 12: Restricting Approximation

## Slide 13: Restricting Approximation

## Slide 14: Restricting Approximation

## Slide 15: Restricting Approximation Globally
module full_adder(a, b, c_in, c_out, s);
…
approximate output s;
relax (s);
…
endmodule
…
restrict_global(s[31:0]);

## Slide 16: Restricting Approximation Globally
module full_adder(a, b, c_in, c_out, s);
…
approximate output s;
relax (s);
…
endmodule
…
restrict_global(s[31:0]);

## Slide 17
Reuse Annotations

## Slide 18: Outputs Carrying Approximate Semantics

## Slide 19: Critical Inputs
…
critical input reset;
critical input clock;
…
Next State Logic
State Register
reset
clock
Output Logic

## Slide 20: Bridging Approximate Wires to Critical Inputs
…
and a1(s, a0, a1);
relax (s);
bridge (s);
multiplexer m0(s, a0, a1, out);
…

## Slide 21: Bridging Approximate Wires to Critical Inputs
…
and a1(s, a0, a1);
relax (s);
bridge (s);
multiplexer m0(s, a0, a1, out);
…

## Slide 22: Baseline Synthesis Flow
Highest frequency with minimum power and area

## Slide 23: Relaxability Inference Analysis
Identify the wires which are driving unannotated wires or annotated with restrict within the module under analysis
Marks any wire that affects a globally restricted wire as precise
Identify the relaxed outputs of the instantiated submodules
Safe to approximate gates
Circuit under analysis with Axilog annotations

## Slide 24: Approximate Synthesis Flow
Axilog Code
Axilog Compiler
Safe to Approximate Gates

## Slide 25: Measurements
Tools for Synthesis and Energy Analysis
Synopsys Design Compiler
Timing Simulation with SDF back annotations
Cadence NC-Verilog
Standard Cell Library
TSMC 45-nm multi-Vt
Synopsys Primetime
Slowest PVT corner (SS, 0.81V, 0C) for baseline results

## Slide 26
FIR # lines: 113
Signal Processing
# Annotations
Design: 6
Reuse: 5
InverseK # lines: 22,407
Robotics
# Annotations
Design: 8
Reuse: 4
ForwardK # lines: 18,282
Robotics
# Annotations
Design: 5
Reuse: 4
K-means # lines: 10,985
Machine Learning
# Annotations
Design: 7
Reuse: 3
Brent-Kung
# lines: 352
Arithmetic Computation
# Annotations
Design: 1
Reuse: 1
26
Benchmarks Arithmetic Computation, Signal Processing, Robotics, Machine Learning, Image Processing
Kogge-Stone # lines: 353
Arithmetic Computation
# Annotations
Design: 1
Reuse: 1
Wallace Tree # lines: 13,928
Arithmetic Computation
# Annotations
Design: 5
Reuse: 3
Neural Network # lines: 21,053
Machine Learning
# Annotations
Design: 4
Reuse: 3
Sobel # lines: 143
Image Processing
# Annotations
Design: 6
Reuse: 3

## Slide 27: Energy Reduction
Chart: Energy Reduction
| Brent-Kung | FIR | ForwardK | InverseK | K-means | Kogge-Stone | Wallace Tree | Neural | Sobel | Geomean
 | 1.2996 | 1.0468 | 1.6247 | 1.7834 | 1.4776 | 1.197 | 1.5353 | 1.7353 | 1.4794 | 1.4451
 | 0.037409 | 0.067982 | 0.16001 | 0.088945 | 0.21689 | 0.044854 | 0.11111 | 0.093656 | 0.091789 | 0.097956
Error ≤ 10%
Error ≤ 5%

## Slide 28: Area Reduction
Chart: Area Reduction
| Brent-Kung | FIR | ForwardK | InverseK | K-means | Kogge-Stone | Wallace Tree | Neural | Sobel | Geomean
 | 2.2765 | 1.032 | 1.7906 | 2.033 | 1.8395 | 1.5396 | 2.186 | 2.0442 | 1.7614 | 1.7921
 | 0.034143 | 0.034804 | 0.18234 | 0.11072 | 0.056872 | 0.065216 | 0.035073 | 0.22978 | 0.054751 | 0.08625
Error ≤ 10%
Error ≤ 5%

## Slide 29: Output Quality Degradation in Sobel
10% Quality loss is nearly indiscernible to the eye Yet provides 57% energy savings
0% Quality Loss
5% Quality Loss
10% Quality Loss

## Slide 30: Energy Reduction for Different PVT Corners
Chart: Energy Reduction
| Brent-Kung | FIR | ForwardK | InverseK | K-means | Kogge-Stone | Wallace Tree | Neural | Sobel | Geomean
 | 0.34 | 0.11 | 0.78 | 0.87 | 0.69 | 0.24 | 0.65 | 0.83 | 0.57 | 0.54
 | 0.32 | 0.07 | 0.72 | 0.79 | 0.65 | 0.21 | 0.63 | 0.72 | 0.41 | 0.48
(SS, 0.81V, 125°C)
(SS, 0.81V, 0°C)

## Slide 31
Axilog
54%
Energy Savings
1.9×
Area Reduction
2-12
Code Annotations
First HDL for Approximation
  Design
  Reuse
  Automation
  High-level
  Backward-compatibility
http://www.act-lab.org/artifacts/axilog