## Slide 1
GRATER: An Approximation Workflow for Exploiting Data-Level Parallelism in FPGA Acceleration
NSF Variability Expedition
Atieh Lotfi, Abbas Rahimi, Amir Yazdanbakhsh, Hadi Esmaeilzadeh, Rajesh K. Gupta UC San Diego, UC Berkeley, Georgia Institute of Technology

## Slide 2: Outline
Motivation
OpenCL Execution Model
Approximation Design Workflow
Experimental Setup and Results
Conclusion

## Slide 3: Motivation
The effective end of Dennard scaling
Performance
Generality
Efficiency
✓Programmable accelerators (FPGAs)
✓Approximate computing
Solutions that provide significant performance and efficiency gains while retaining generality is needed

## Slide 4: Motivation
Image Processing
Big Data Analytics
Multimedia
Machine Learning
Web Search
✓ Can benefit from FPGA acceleration
✓ Tolerance to imprecise computing
An automated design workflow is to bridge the gap between approximation and FPGA acceleration
GRATER
Quality
Performance

## Slide 5: Our Contributions
Automatically leverages approximation to utilize data-level parallelism and achieve higher throughput for FPGA accelerators
Uses a source-to-source compiler to systematically tune the precision of operations and data in an OpenCL kernel
Exploits a genetic-based pre-synthesis optimization to reduce the synthesized kernel area while statistically satisfying the QoR target

## Slide 6: Outline
Motivation
OpenCL Execution Model
Approximation Design Workflow
Experimental Setup and Results
Conclusion

## Slide 7: OpenCL Platform Model
…
…
…
…
…
…
…
…
…
Processing Element
Compute Unit (CU)
Compute Device
Host
Host Code
Kernel Code
Work-item

## Slide 8: Mapping OpenCL Programs on FPGAs
Altera OpenCL SDK
GPUs and FPGAs exploit data-level parallelism differently:
  GPUs: SIMD in a CU
  FPGAs: pipeline parallelism in a CU
FPGAs can improve throughput by creating multiple copies of the kernel pipelines
  Our aim is to increase the number of pipeline copies in a fixed FPGA chip

## Slide 9: Outline
Motivation
OpenCL Execution Model
Approximation Design Workflow
Experimental Setup and Results
Conclusion

## Slide 10: GRATER: Approximation Design Workflow
2. Genetic-based Approximation Algorithm
FPGA
HLS tool
(OpenCL to RTL)
Quality Metric
Test cases
Mutation/
Crossover
Fitness evaluation
Selection
Population
(Modified kernel)
GPU
accelerated profiling
Exact
OpenCL kernel
Approximate kernel
Least Area
Acceptable QoR
Source-to-source compiler
1. Analysis and Pruning
Automatically reduces the precision of kernel’s variables (and operations)
e.g. float->{int, short, char}

## Slide 11: Source-to-source Compiler Analysis and Pruning
Detect variables amenable to approximation (AV)
Find lowest possible precision(LP) for each
Generate with all replaced by LPi
Run on GPU
QoR
passed?
Run genetic-based algorithm
 Solution found:
Yes
No
Assign a precision tag (𝑷𝑻) to each variable type: e.g. data types {float, int, short, char} -> {4, 3, 2, 1}

## Slide 12: Source-to-source Compiler Genetic-based Approximation Algorithm (1/3)
Genetic Representation of Chromosomes
;
Chromosome Candidate approximate kernel
All individuals in the population must meet the desired QoR.
Candidate approximate kernel QoR check can be verified:
  By execution (accelerated on a GPU), or
  Without execution (comparing its PT values with the least precision chromosome found)
PTV1 | PTV2 | PTV3 | …. | PTV¦AV¦
1-to-1 correspondence

## Slide 13: Source-to-source Compiler Genetic-based Approximation Algorithm (2/3)
Which individuals would survive to the next generation?
Fitness Function:
    Objective: Finding an approximate kernel that minimizes resource utilization on FPGA while meeting the QoR.
            = 0, 1, 2, 6 for PT=1, 2, 3, 4
  The lower the fitness value, the lower area occupancy that configuration has

## Slide 14: Source-to-source Compiler Genetic-based Approximation Algorithm (3/3)
Genetic Operators
  One-point crossover
  Mutation
  Selection
  Chromosomes are sorted based on their estimation of fitness value in each iteration
  Elitism selection + Proportionate selection
PTV1 | PTV2 | …. | …. | PTVn
PTV1 | PTV2 | …. | …. | PTVn
PTV1 | PTV2 | …. | …. | PTVn
PTV1 | PTV2 | …. | …. | PTVn
Random crossover point
PTV1 |  | …. |  | …. | PTVn
PTV1 | PTV2’ | …. | PTVk’ | …. | PTVn
Random points

## Slide 15: Outline
Motivation
OpenCL Execution Model
Approximation Design Workflow
Experimental Setup and Results
Conclusion

## Slide 16
OpenCL AMD APP SDK v2.9 benchmark
  Image Processing (recursive gaussian, sobel)
  Signal Processing (convolution, dct)
  Physical Simulation (n-body)
AMD Evergreen Radeon HD 5870 GPU device for accelerated profiling experiments
Kernels were synthesized for Altera DE5 board with a Stratix V FPGA using Altera OpenCL SDK 13.1 synthesis tool
100 training inputs and 100 test inputs
Experimental Setup
Image Processing, Signal Processing, Physical Simulation

## Slide 17: Experimental Results Area Savings with Approximate Kernels
Chart: 
| r-gaussian | sobel | dct | conv | n-body | geomean
Exact | 5 | 5 | 8 | 15 | 3 | 6
Approximate | 9 | 13 | 11 | 21 | 10 | 12
No. of Mapped Kernels
Reduction in resource utilization for 1 mapped kernel (14%–25%)
Increase in number of mapped kernels on FPGA (2x on average)
Logic: 96%
DSP: 91%
RAM: 91%
Logic: 92%
DSP: 93%

## Slide 18: Experimental Results Speedup
Chart: 
| r-gaussian | sobel | dct | conv | n-body | geomean
GPU | 1.1074 | 1.011 | 1.0236 | 1.0261 | 1.1818 | 1.068
FPGA | 1.71 | 2.0226 | 1.3658 | 1.4108 | 2.9756 | 1.8179
Speedup (Improved Throughput)
Increase in FPGA throughput (1.82x on average)
Increase in GPU speedup (1.07x on average)

## Slide 19: Experimental Results Quality Loss
Chart: 
| r-gaussian | sobel | dct | conv | n-body | geomean
Series 1 | 4.5e-06 | 8.0141e-05 | 0.0003874 | 0.00058 | 0.0003 | 0.00028041
Average Quality Loss
Average quality loss over 100 test input patterns is ≤ 1%

## Slide 20: Conclusion
GRATER exploits approximation to increase the benefits of FPGA accelerators without changing the underlying FPGA hardware
More opportunities for parallel execution
1.4x–3.0x higher computational throughput on FPGA with less than 1% quality loss

## Slide 21
GRATER : An Approximation Workflow for Exploiting Data-Level Parallelism in FPGA Acceleration
1.8x Speedup 99% Quality
(1.4x–3.0x)
Atieh Lotfi, Abbas Rahimi, Amir Yazdanbakhsh, Hadi Esmaeilzadeh, Rajesh K. Gupta UC San Diego, UC Berkeley, Georgia Institute of Technology
GRATER

## Slide 22: Source-to-source Compiler Genetic-based Approximation Algorithm
Modified kernel
Initial population
…
Fitness evaluation
Selection
(Elitism, roulette wheel )
Crossover / Mutation
Termination
criterion?
Yes
Next Generation
Accelerated Profiling
…
No
Solution 
(kernel with the least area)
Variable precision
Satisfy
QoR
Estimates kernel area
occupancy on FPGA

## Slide 23: Source-to-source Compiler Analysis and Pruning
Assign a precision tag () to each variable type: e.g. data types {float, int, short, char} -> {4, 3, 2, 1}
Detect variables amenable to approximation (): by one demoting for each and checking the QoR
Find lowest possible precision for each (): starting from char for each and performing one promoting until it satisfies the QoR (generating |AV| kernels)
Generate for all
  Run on GPU and check the QoR
  if QoR > Quality_Target: solution is found ()
  otherwise: run genetic-based algorithm