## Slide 1
University of California San Diego
*University of California Berkeley
Mohsen Imani, Abbas Rahimi*, Tajana S. Rosing
Resistive Conﬁgurable Associative Memory for Approximate Computing

## Slide 2: Motivation
Internet of Things (IoT):
  Billions~Trillions of interconnected devices (large scale problem)
  Amount of data generation in 2011 1.8 zettabytes which will be increased by 50% in 2020!
Battery powered  tight energy efficiency requirements
Materials
Technology
Components
Architecture
Operating System
Software

## Slide 3: Motivation
Processor Pipeline
Look up Table
MEM
Input operands
Clock gating
Internet of Things (IoT):
  Billions~Trillions of interconnected devices (large scale problem)
  Amount of data generation in 2011 1.8 zettabytes which will be increased by 50% in 2020!
Battery powered  tight energy efficiency requirements
A promising solution: use of associative memories
Not a new technique, but a new application field!
Result of computation
Matching?
Requirements: low area, low energy, fast

## Slide 4: Related Work
Energy efficient computation
Energy efficient computing units
Associative memory
(“Computation with memory”) [Kohonen 2012]
CMOS-based [Lakshminarayanan 2005]
NVM-based [Li 2012]
Exact matching [Rahimi 2014]
Approximate matching (VOS) [Rahimi 2015]
Energy efficient resistive associative memories !
Memrist [Li 2012]
MTJ [Matsunaga 2012]
Lower energy consumption
Higher search speed and area efficiency
Lower energy consumption (at the cost of accuracy)
VOS: Voltage OverScaling

## Slide 5: Resistive Associative Memory (1/2)
Number of rows
Word size
Processor Pipeline
Look up Table
MEM
Input operands
Clock gating
Result of computation
TCAM: Ternary Content Addressable Memory
Energy saving is proportional to hit rate
The higher the TCAM size, the higher hit rate
GOAL: Lower TCAM energy to achieve higher energy efficiency
Row
Cell

## Slide 6: Resistive Associative Memory (2/2)
Limitations of conventional Resistive TCAM:
  Word size
  Number of rows
  Search energy
Long word  High leakage current
Lots of rows  Large and energy hungry input buffers
Input Buffer
Search operation  All TCAM rows require precharging
Vdd
Low Energy TCAM
Higher
Hit Rate
Online Profiling
Energy
Solutions?
Approximation

## Slide 7: Profiling (1/3)
Hit rate
Larger TCAM
Energy limitation 
Online profiling
Cost of profiling?
How much energy improvement can we achieve with online profiling?
Is it worth to accept profiling cost?

## Slide 8: Profiling (2/3)
Considered Oracle as the best case representation of online profiling
  Oracle: Trained on 100% of dataset, and then tested
  Train-test: trained on 10%, and tested on 100% of dataset
Oracle achieves up to 18% higher hit rate!
Is Oracle hit rate improvement enough for online profiling?
Sobel

## Slide 9
Profiling (3/3)
Comparing the best energy point of Oracle and Train-test profiling
Repeating the experiment on 8 different applications
Oracle results in 15% higher energy efficiency!
9

## Slide 10: TCAM with Approximate Search (1/2)
TCAMs under VoS accept hamming distance matching
Faster reads or lower supply voltages subject to controllable approximate matching
  1000mv: Exact Matching
  775mv: 1-HD Matching
  720mv: 2-HD Matching
Precharge
Evaluation
Precharge
Evaluation
Precharge
Evaluation
1000mV
775mV
725mV

## Slide 11: TCAM with Approximate Search (2/2)
Advantages:
  Lower TCAM search energy, lower swing 
  Lower FPU energy 
    Higher hit rate
    Increases average clock gating rate
  Disadvantages:
  No difference between MSB and LSB bits  Loss of accuracy 
    Just provides enough accuracy on a few Multimedia applications
    Limits the TCAM size (# of rows)

## Slide 12: Contributions
State-of-the-art: Single-stage resistive associative memory
ReCAM: Resistive Configurable Associative Memory
  Composed of a TCAM + Memory
  Is tightly-integrated with FPU
  Prioritize the TCAM mismatches on LSBs rather than MSBs
  Fast configurable TCAM architecture (~5ns)
  Reduces GPU energy consumption by up to 45%

## Slide 13: AMD GPU Architecture
Radeon HD 7970 device from Southern Islands family
  32 compute units
    4 SIMD units
      16 stream cores (parallel lanes)
2048 stream cores per device
Thermal design power: 300W!
Local Memory
Wavefront Scheduler
Compute Unit
SIMD Unit 1
SIMD Unit 2
SIMD Unit 3
SIMD Unit 4
Ultra-threaded Dispatcher
Compute Unit 1
Compute Unit 32
Global Memory
Compute Device
…
IF/ID
Vector/Scalar RF
SIMD Unit
Stream Core 16
Stream Core 1
Stream Core 2
Stream Core 3
…

## Slide 14
Associative Memory Integration

## Slide 15: ReCAM Architecture
Solution: Split the TCAM in stages
Applying VoS on the selective blocks
What about
  # of stage?
  Level of voltage?
1
2
MSBs
Input Buffer
3
Sense amp.
LSBs
N/m bits
Less impact on accuracy

## Slide 16: ReCAM: Bitline Approximation
ShortStop [Pinckney’13] technique to put the blocks under approximation
Each Block can approximate individually
Approximation starts from lease significant blocks
Adaptive Architecture in 5ns!
1
2
MSBs
Input Buffer
3
Sense amp.
LSBs

## Slide 17: ReCAM: Row Approximation
First TCAM rows has more probability of hit rate  high error rate in case of approximation
Partitioned TCAM to row blocks and apply selective approximation
VoS starts from last rows
1
2
Input Buffer
3
Sense amp.

## Slide 18: ReCAM Framework
Number of block in approximation
  Application type
  Acceptable accuracy of loss (10% average relative error in this case [Esmaeilzadeh’12]
    Tradeoff between the energy and accuracy
  - Adaptive architecture!

## Slide 19: Experimental Setup
AMD GPUs
  Image processing applications from AMD APP SDK v2.5
  Multi2Sim for AMD Southern Islands GPU, Radeon HD 7970 device
  OpenCL applications: Sobel, Robert, Sharpen, Shift
FPU ASIC flow
  6-stage balanced FPUs generated by FloPoCo
  Synthesized and mapped using a 45-nm TSMC
  Optimized for power and a clock period based on TCAM delay:
    Synopsys Design Compiler
    FPU power estimation: Synopsys PrimeTime (1.0V)
ReCAM design flow
  Transistor-level HSPICE simulations for power and delay using 3T-1R TCAM cell [Chang’15]

## Slide 20: ReCAM Size
What’s the best ReCAM size?!
ReCAM Size
Hit rate
TCAM energy
FPU: average clock gating time
TCAM delay
Solution?
Parallel search
Solution?
ReCAM approximation

## Slide 21: Experimental Results
GPGPU Energy Consumption:
  Trade-off between FPU and TCAM energy consumption
  Minimum point: tradeoff between FPU and TCAM consumption
  Energy saving compared to GPU alone:
GPU + Exact Matching ReCAM | + 24%

## Slide 22: Experimental Results
ReCAM approximation:
  Maximum number of blocks (bitline/rows) under 1-HD or 2-HD approximation
  Acceptable quality of service (10% average relative error)
Sobel- bitline Approximation
GPU + Bitline Approximate ReCAM | 43%
GPU + Row Approximate ReCAM | 45%
Sobel – Row Approximation
2-HD
1-HD
1-HD
2-HD
Average energy saving over 8 applications

## Slide 23: Conclusion
Approximation is a technique to reduce energy at the cost of computation inaccuracy
Fine grained approximation tuning is required to adaptively relax the computation of different application
  Proposed ReCAM is Resistive Configurable Associative Memory which relaxes computation in both row and bitline views
  Goal: energy saving with minimum impact on inaccuracy
  ReCAM integration with GPU results in 45% energy efficiency on average over eight GPGPU applications