## Slide 1: WILD: A Workload-Based Learning Model to Predict Dynamic Delay of Functional Units
Xun Jiao*, Yu Jiang+, Abbas Rahimi$, and Rajesh K. Gupta*
*University of California, San Diego
+Tsinghua University
$University of California, Berkeley

## Slide 2: Agenda
Motivation
Our Methodology
Experimental Results
Conclusions

## Slide 3: STA-induced Performance Loss
Static Timing Analysis:
  Delay of critical path  Conservative timing margin
  In reality, critical path not sensitized  shorter delay < Tclk
  Dynamic path analysis  real delay?
Dynamic Slack

## Slide 4: Instruction-level Dynamic Analysis
[roy2012predicting], [xin2011identifying], [constantin2015exploiting]
Measure worst delay for instructions:
  For example, 1ns for ADD, 2ns for DIV…
Overlooks the impact of input operands
Need to consider operand for path sensitization
We firstly propose to use machine learning methods to predict the dynamic delay for a given input operands, considering the impact of operands on dynamic path sensitization.
INT_ADD
Worst delay
Wide range of delay

## Slide 5: Agenda
Motivation
Our Methodology: WILD Model
  Problem Formulation and Overview
  Three Key Phases
Experimental Results
Conclusions

## Slide 6: Problem Formulation
Learn relationship between input operands and dynamic delay.
x[1],x[2]…x[t-1],x[t]
D[t]
Cycle t:
Model
Solve three problems:
Measure the dynamic delay at each cycle;
Identify input features from operands;
Learn the mapping relationship.

## Slide 7: Overview
Application
Architecture Simulator
Workload Signature
RTL Description
Synthesis
Place & Route
Gate-level Simulation
Feature Extraction
TSMC 45nm
Gate-level Netlist
Switching
Activity
Dynamic Timing Analysis
Model
Training
b) Input Feature
Extraction
a) Dynamic Timing Analysis
Random Data Generator
Dynamic Delay
c) Model Training
Input Feature
Three key phases:
Dynamic Timing Analysis  dynamic delay;
Input Feature Extraction  input feature;
Model Training  learning model.

## Slide 8: Agenda
Motivation
Our Methodology: WILD Model
  Problem Formulation and Overview
  Three Key Phases
    Dynamic Timing Analysis
    Input Feature Extraction
    Model Training
Experimental Results
Conclusions

## Slide 9: Dynamic Timing Analysis
Application
Architecture Simulator
Workload Signature
RTL Description
Synthesis
Place & Route
Gate-level Simulation
Feature Extraction
TSMC 45nm
Gate-level Netlist
Switching
Activity
Dynamic Timing Analysis
Model
Training
b) Input Feature
Extraction
a) Dynamic Timing Analysis
Random Data Generator
Dynamic Delay
c) Model Training
Input Feature
RTL description | An open-source tool: Flopoco
Synthesis | Synopsys Design Compiler
Place&Route | Synopsys IC Compiler
Gate-level Simulation | Mentor Graphics Modelsim
Dynamic Timing Analysis | Python-Written VCD Analysis Script

## Slide 10: Dynamic Timing Analysis
We parse and analyze VCD file to measure the dynamic delay at each cycle.
Wrapper
Wrapper
x1[31:0]
x2[31:0]
CLK
……
……
y[0]
y[1]
y[31]
y[31:0]
Measure dynamic delay at each cycle:
Run gate-level simulation at a safe clock period;
Dump the toggling activity of endpoints(y[0],…y[31]) at each cycle via VCD file;
Locate the last toggle event time at cycle ;
Locate last positive clock edge .
Compute delay at each cycle: .

## Slide 11: Agenda
Motivation
Our Methodology: WILD Model
  Problem Formulation and Overview
  Three Key Phases
    Dynamic Timing Analysis
    Input Feature Extraction
    Model Training
Experimental Results
Conclusions

## Slide 12: Input Feature Extraction
Application
Architecture Simulator
Workload Signature
RTL Description
Synthesis
Place & Route
Gate-level Simulation
Feature Extraction
TSMC 45nm
Gate-level Netlist
Switching
Activity
Dynamic Timing Analysis
Model
Training
b) Input Feature
Extraction
a) Dynamic Timing Analysis
Random Data Generator
Dynamic Delay
c) Model Training
Input Feature
Random Data Generator | Python-Written Script
Application | Sobel filter, Gaussian filter from AMD APP SDK v2.5. Input images from Caltech-UCSD Birds 200 vision datasets.
Arch-Simulator | Modified Multi2Sim
Workload Signature | Data preprocess
Feature Extraction | Trial-and-error process

## Slide 13: Input Feature Extraction
Data preprocessing:
  Decimal  Binary
  Remove repetitive pattern
Clean binary vector
Question remains:
For D[t] at cycle t, will the history input x[t-1], x[t-2], … have impact on it?

## Slide 14: Input Feature Extraction
Trail-and-error process:
  Scenario 1: fix x[t], vary x[t-1]
  Scenario 2: fix x[t] and x[t-1], vary x[t-1]
Preceding input set an state, current input toggle the state.
Input feature: {x[t], x[t-1]}.
 D[t] changed
 D[t] constant

## Slide 15: Agenda
Motivation
Our Methodology: WILD Model
  Problem Formulation and Overview
  Three Key Phases
    Dynamic Timing Analysis
    Input Feature Extraction
    Model Training
Experimental Results
Conclusions

## Slide 16: Model Training
Application
Architecture Simulator
Workload Signature
RTL Description
Synthesis
Place & Route
Gate-level Simulation
Feature Extraction
TSMC 45nm
Gate-level Netlist
Switching
Activity
Dynamic Timing Analysis
Model
Training
b) Input Feature
Extraction
a) Dynamic Timing Analysis
Random Data Generator
Dynamic Delay
c) Model Training
Input Feature
Input Feature | 
Dynamic Delay | 
Model Training | Supervised learning methods

## Slide 17: Model Training
2.5ns is the clean clock period for all designs, so we classify the delay into five classes:
To train the model, we apply various learning methods to these training data.

## Slide 18: Model Evaluation
Evaluation metric: prediction accuracy.
Comparison methods:
  rand: randomly predict the delay class among the non-empty classes.
  naive: always predict the class which contains the most instances.
    high accuracy for biased datasets.

## Slide 19: Agenda
Motivation
Our Methodology
Experimental Results
Conclusions

## Slide 20: Delay Distribution of FUs
INT_ADD
INT_MUL
FP_MUL
Facts:
  FUs exhibit wide range of delay;
  APP’s data locality.
Worst delay

## Slide 21: Model Prediction Accuracy
Facts:
  WILD achieves accuracy ranging 96.2~99.8%.
  WILD achieves 98.0% on average.
  rand achieves 27.2% on average, always low.
  naive achieves 63.6% on average, could be high.

## Slide 22: Instruction-level Timing Margin Reduction
Existing model uses worst delay.
WILD uses the predicted delay class.
  Misprediction: performance penalty.
AVERAGE INSTRUCTION-LEVEL TIMING DELAY(PS) USING WILD COMPARED TO EXISTING
INSTRUCTION-LEVEL TIMING MODEL

## Slide 23: Agenda
Motivation
Our Methodology
Experimental Results
Conclusions and Discussions

## Slide 24: Discussions
Overhead of WILD:
  Hardware overhead: This model is enabled by logistic regression, less complex than SVM-based model in [ye2014chip].
  Timing overhead: WILD is 60X faster than gate-level simulation.

## Slide 25: Conclusions
WILD is a supervised learning model to predict dynamic delay of FUs for a given input workload.
WILD exhibits high prediction accuracy and fast execution speed.

## Slide 26: THANK YOU !