## Slide 1: An EMG Gesture Recognition System with Flexible High-Density Sensors and Brain-Inspired High-Dimensional Classifier
Ali Moin∗, Andy Zhou∗, Abbas Rahimi∗†, Simone Benatti‡, Alisha Menon∗, Senam Tamakloe∗, Jonathan Ting∗, Natasha Yamamoto∗, Yasser Khan∗, Fred Burghardt∗, Luca Benini†‡, Ana C. Arias∗, Jan M. Rabaey∗
∗UC Berkeley, †ETH Zurich, and ‡University of Bologna

## Slide 2: Outline
High-dimensional (HD) Computing
  Mapping to HD Space
  HD Arithmetic
  Generic HD Processing Unit
Electromyography (EMG)-based Hand Gesture Recognition
  System Components for Flexible EMG
  Fast and one-shot learning

## Slide 3: Brain-inspired High-dimensional Computing
Emulation of cognition by computing with high-dimensional (HD) vectors [P. Kanerva, Cogn Comput’09]
Most of the HD space is nearly orthogonal to any given point
Supports full algebra
Superb properties for nanoscalable computing paradigms [TCAS-I’17]:
General and scalable model of computing
Well-defined set of arithmetic operations
Fast and one-shot learning (no need of back-prop)
Memory-centric with embarrassingly parallel operations
Purely statistical, thrives on randomness
Extremely robust against most failure mechanisms and noise
Chart: 
99.9999998% of the space lies at approximately
the mean distance [0.47,0.53] from a point
0.53
0.47

## Slide 4: What Are HD Vectors? It is all about data representation
1st 2nd 3rd 4th 10000th
[−1 +1 −1 −1 .............. +1]
Combine and Compare
Approximate computation with fixed-size long random patterns that provides a novel look at data representations, associated operations, circuits, and architectures.
High-dimensional
Holographic
Distributed
Pseudorandom with i.i.d. components
binary
bipolar
dense
sparse

## Slide 5: Mapping to HD Vectors
Each “symbol” (e.g., a channel in EMG) is represented by an HD vector chosen at random with 10,000−d:
  E1 = [−1 +1 −1 −1 −1 +1 −1 −1 ...]
  E2 = [+1 −1 +1 +1 +1 −1 +1 −1 ...]
  E3 = [−1 −1 −1 +1 +1 −1 +1 −1 ...]
  E4 = [−1 −1 −1 +1 +1 −1 +1 −1 ...]
  ...
  E64 = [−1 −1 +1 −1 +1 +1 +1 −1 ...]
Every HD vector is dissimilar to others: ⟨E1,E2⟩ = 0
This assignment is fixed throughout computation
Item Memory (IM)
“Electrode 1”
E1
6
10,000

## Slide 6: HD Arithmetic
Componentwise addition (+) is good for representing sets, since sum vector is similar to its constituent vectors:
  ⟨A+B,A⟩ = 0.5
Componentwise multiplication (∗) is good for binding, since product vector is dissimilar to its constituent vectors:
  ⟨A∗B,A⟩ = 0
Random permutation (ρ) is good for representing sequences, since permuted vector is dissimilar:
  ⟨A,ρA⟩ = 0
∗ and ρ are invertible and preserve distance

## Slide 7: Generic HD Processing Unit Identical hardware for both learning and inference
Maps input vectors into d-dimensional (d≈10,000) pseudo-orthogonal random vectors Nanodevice opportunity to exploit process randomness and utilize variability
Encodes all input information into single HD vector
using simple local operators (∗,+,ρ)
Finds closest match in trained data
Can be continuously updated
Associative Memory
Seed Generation
HD Encoder
d
HD vectors
HD Space
m
Preprocessing/
Transformations
Inputs
LD Space
Outcomes
k
LD Space
d
HD vectors
Part of preprocessing can be eliminated

## Slide 8: HD Processing for Gesture Recognition
Preprocessing Chain

## Slide 9: HD Processing for Gesture Recognition
Preprocessing Chain
Spatial Encoding

## Slide 10: HD Processing for Gesture Recognition
Preprocessing Chain
Spatial Encoding
Temporal Encoding

## Slide 11: HD Processing for Gesture Recognition
Preprocessing Chain
Spatial Encoding
Temporal Encoding
Train

## Slide 12: HD Processing for Gesture Recognition
Preprocessing Chain
Spatial Encoding
Temporal Encoding
Train
Test

## Slide 13: Many Variants of Same …
Applications | #I | #C | HD | Baseline
Language identification [ISLPED’16] | 1 | 21 | 96.7% | 97.9%
Text categorization [DATE’16] | 1 | 8 | 94.2% | 86.4%
Speech recognition [ICRC’17] | 1 | 26 | 95.3% | 93.6%
EMG gesture recognition [ICRC’16] | 4 | 5 | 97.8% | 89.7%
Flexible EMG [this work] | 64 | 5 | 96.6% | 88.9%
EEG brain-machine interface [BICT’17] | 64 | 2 | 74.5% | 69.5%
2× lower energy than SVM
Embedded Accelerator (28nm, 1.5mm2, 2mW) [DAC’18]
256 channels: 10 ms real-time constraints
10× lower energy than ARM Cortex-M4

## Slide 14: System Components for Flexible EMG
Sensory Array
(Flex)
Data Acquisition
(Up to 128 channels)
~2 Mbps Wireless Link
Front Side
Or …
Flexible PCB 4x16 Array
(29.3 cm × 8.2 cm)
HD Classification (This work)
Fine-grained coverage of muscular surface
Back Side

## Slide 15
One-shot: 89.2%
Train/Test 30 mins apart
With repositioning: 82%
SVM: 51%
Train/Test 1 day apart
HD Learns Fast

## Slide 16: Summary
Key properties of HD computing:
  a versatile set of arithmetic operations, generality, scalability, robustness, and fast one-shot learning
A prime candidate for wearable biosignal processing, in which
  signals are noisy and nonstationary
  training data sets are not huge
  individual variability is significant
  energy efficiency constraints are tight
Dataset and codes available at https://github.com/a-moin/flexemg

## Slide 17
Thanks!