## Slide 1: A Robust and Energy-Efficient Classifier Using Brain-Inspired Hyperdimensional Computing
Abbas Rahimi, Pentti Kanerva, Jan M. Rabaey
UC Berkeley

## Slide 2: Outline
Background in HD Computing
Language Recognition as an Example
HD Memory-centric Architecture
Experimental Results
  Classification Accuracy
  Memory footprint and Energy
  Robustness

## Slide 3: Brain-inspired Hyperdimensional Computing
HD computing:
Representation with dimension “much” (> 10,000) larger than needed to cover space
Purely statistical, thrives on randomness
Information distributed in space
Supports full algebra
Superb properties:
General and scalable model of computing
One-shot learning
Memory-centric with embarrassingly parallel operations
Extremely robust against most failure mechanisms and noise
[P. Kanerva, An Introduction to Computing in Distributed Representation with High-Dimensional Random Vectors, 2009]

## Slide 4: What Are Hypervectors?
  Patterns as basic data representation in contrast to computing with numbers!
Hypervectors are:
  high-dimensional (e.g., 10,000 dimensions)
  (pseudo)random with i.i.d. components
  holographically distributed (i.e., not microcoded)
Hypervectors can:
  use various coding: dense or sparse, bipolar or binary
  be compared for similarity using distance metrics
  be combined using arithmetic operations: multiplication, addition, and permutation

## Slide 5: Mapping to Hypervectors
Each symbol is represented by a 10,000-D hypervector chosen at random:
A = -1 +1 -1 -1 -1 +1 -1 -1 ...
B = +1 -1+1 +1+1 -1 +1 -1 ...
C = -1 -1 -1 +1 +1 -1 +1 -1 ...
D = -1 -1 -1 +1 +1 -1 +1 -1 ...
...
Z = -1 -1 +1 -1 +1 +1 +1 -1 ...
Every letter hypervector is dissimilar to others, e.g., ⟨A, B⟩ = 0
This assignment is fixed throughout computation
Item Memory
“a”
A
8
10,000

## Slide 6: HD Arithmetic
  MAP operations:
  Multiplication (*) is good for binding, since product vector is dissimilar to its constituent vectors: ⟨A*B, A⟩=0
  Addition (+) is good for representing sets, since sum vector is similar to its constituent vectors: ⟨A+B, A⟩=0.5
  Permutation (ρ) is good for representing sequences, makes a dissimilar vector by rotating: ⟨A, ρA⟩=0
  * and ρ are invertible and preserve the distance

## Slide 7: Example Problem
Identify the language from a stream of letters (n-grams)
Train with a megabyte of text from each of 21 EU languages
Item Memory
dutch
21×10,000-D learned language hypervectors
Encoding:
MAP operations
Associative Memory
Letter hypervector
10,000-D
Language hypervector
10,000-D
Train text: “ik wil hier en daar een greep uit de geschiedenis doen en ga over...”
Test with 1,000 sentences from each (from independent source)
Item Memory
Identified language
Encoding: MAP operations
Associative Memory
Letter hypervector
10,000-D
Text hypervector
10,000-D
Test sentence: “daher stimme ich gegen anderungsantrag welcher”

## Slide 8: Its Algebra is General: Architecture Can Be Reused
Associative memory
S1
5-bit
10K-bit
Item memory
10K-bit
Hand gestures: 5 classes
S2
5-bit
10K-bit
Item memory
S3
5-bit
10K-bit
Item memory
S4
5-bit
10K-bit
Item memory
Encoder: MAP operations
Associative memory
Letter
8-bit
10K-bit
10K-bit
Languages: 21 classes
Item memory
Encoder: MAP operations
Applications | n-grams | HD | Baseline
Language identification | n=3 | 96.7% | 97.9%
Text categorization | n=5 | 94.2% | 86.4%
EMG gesture recognition | n=3,4,5 | 97.8% | 89.7%

## Slide 9: Computing a Language Profile (1/2)
Random projection of the letters to {-1,+1}10,000
From letters to trigrams (rotate and multiply)
  Trigram: a three-letter sequence
  “the” is encoded by ρρT * ρH * E
From trigrams to a language profile (addition)
  Add all trigram hypervectors into a single 10,000-D hypervector.
  For example, the following trigrams are generated from:
“The car is ready” the he# e#c #ca car ar# r#i #is is# s#r #re rea ead ady
  A megabyte of text produces a profile whose components are integers with mean = 0 and standard deviation = 1,000

## Slide 10: Computing a Language Profile (2/2)
Trigram encoding “the”  ρ ρT * ρH * E
T = +1 -1 -1 +1 -1 -1 ... +1 +1 -1 -1 +1 -1
/ / / / / / / / / / / /
/ / / / / / / / / /
H = +1 -1 +1 +1 +1 +1 ... +1 -1 +1 -1 +1
/ / / / / / / / / / /
/ / / / / / / / /
E = +1 +1 +1 -1 -1 +1 ... +1 -1 +1 +1
-----------------------------------------------
“the”= +1 +1 -1 +1 .... ... +1 +1 -1 -1
Adding trigrams “the car”  “the” + “he#”+ “e#c” + …
“the” = +1 +1 -1 +1 -1 +1 ....
“he#” = -1 -1 +1 +1 -1 +1 ....
“e#c” = -1 -1 +1 +1 +1 -1 ....
“#ca” = +1 -1 +1 -1 -1 -1 ....
“car” = -1 +1 +1 -1 -1 +1 ....
--------------------------------
= -1 -1 +3 +1 -3 +1 ....
“the car”

## Slide 11: Experimental Setup
Language recognition dataset (21 EU languages)
  Train with 1MB of text from Wortschatz Corpora
  21,000 test sentences from Europarl Parallel Corpus
Baseline classifier
  Nearest neighbor classifier that uses histograms of n-grams
SystemVerilog RTL and MATLAB implementations
  Synopsys Design Compiler with TSMC’s 65 nm, LP process, high VTH cells
  Extracting switching activity using ModelSim
  Power consumptions using Synopsys PrimeTime at (1.2V, 25C, TT) corner
Available to download at:
https://github.com/abbas-rahimi/HDC-Language-Recognition

## Slide 12: Memory-centric HD Architecture
Item memory
  Bipolar code  Binary dense code {0,1}10,000
Encoder MAP operations
  Multiplication  XOR
  Addition  Majority rule (accumulation and thresholding)
  Permutation  Fixed cyclic shift to right by 1 position
Associative memory
  Cosine similarity  Hamming distance

## Slide 13: Encoding Trigrams with Lower Switching Activity
Hotspot: encoder has 3X higher switching activity due to shift and XORs
Reducing switching in memory:
  Storing hypervectors in their arrival order
  Three Barrel shifters rotate them before XORs

## Slide 14: Classification Accuracy, Memory, and Energy
 | Accuracy (%) |  | Memory (kB) | 
n-grams | HD | Base | HD | Base
n=2 | 93.2 | 90.9 | 670 | 39
n=3 | 96.7 | 97.9 | 680 | 532
n=4 | 97.1 | 99.2 | 690 | 12837
n=5 | 95.0 | 99.8 | 700 | 373092
Compared to NN baseline:
1.2% lower accuracy with 53% energy saving for trigrams
500× smaller memory size for pentagrams
HD represents many more n-grams within the same hardware structure
High accuracy with binary components:
19× memory reduction for 1.3% lower accuracy (97.4% to 96.7%)

## Slide 15: Robustness Against Memory Errors
Near peek accuracy: HDC tolerates 8.8-fold probability of failure compared to the baseline
Robustness in low SNR:
Seed hypervectors with i.i.d. components
MAP operations are nearly i.i.d.-preserving
Holographic: a failure in a component is not “contagious”
HD algorithm is incremental with no control flow conditions

## Slide 16: Summary
A robust and energy-efficient design for HD computing
  Memory-centric, modular, and scalable architecture
  Embarrassingly parallel and local operations
  One-shot learning
Compared to a conventional NN classifier, HD
  saves 53% energy (w/o harnessing robustness)
  tolerates 8.8-fold probability of failure for individual memory
  classifies 94% of sentences correctly (at max. 3% lower than NN)

## Slide 17: Acknowledgment
This work was supported in part by Systems on Nanoscale Information fabriCs (SONIC), one of the six SRC STARnet Centers, sponsored by MARCO and DARPA.