## Slide 1
†University of California San Diego
‡University of California Berekely
Mohsen Imani†, Yeseong Kim†, Abbas Rahimi‡, Tajana S. Rosing†
ACAM: Approximate Computing Based on Adaptive Associative Memory with Online Learning

## Slide 2: Motivation
Internet of Things (IoT):
  Billions-trillions of interconnected devices (large scale problem)
  1.8 zettabytes of data generated in 2015, increased by 50% in 2020!
  Battery powered  tight energy efficiency requirements
Solution: Approximate computing gets results faster, at lower energy cost and with sufficient accuracy!
  Inaccuracy is inherent => most applications do not need exact results
    E.g. machine learning, speech recognition, search, graphics, etc.

## Slide 3: Associative Memory
Processor Pipeline
Look up Table
MEM
Input operands
Clock gating
Associative memories: a promising solution to reduce energy consumption of parallel processors
Prestores high frequency patterns and their corresponding outputs
Result of computation
Matching?
Requirements: low area, low energy consumption, high performance
TCAM: Ternary Content Addressable Memory

## Slide 4: Related Work
Energy efficient computation
Energy efficient computing units
Associative memory
(“Computation with memory”)
CMOS-based [Ullah TCAS’12] [Pagiamtzis ISSCC’06][Arsovski JSSC’03]
NVM-based [Li ISSCC’14], [Chang ISSCC’15], [Huang VLSIC’14] [Govindaraj JLPED’15]
Exact/Approximate matching
[Zhang DAET’15],[Rahimi DAC’14]
Memoization
Approximate Computing
Associative Computing
[Guo ISCA’13] ,[Rahimi DATE’15] [Imani DATE’16],[Sharad DAC’13]
Memristor
MTJ
Notes: Explain non-volatile memory
Which non-volatile did u use?
Define VOS
Which NVM, why?!
Focuse on tunable

## Slide 5: Associative Memory Energy Solution
Hit rate
Online profiling
Cost of profiling?
Energy Solution
Energy efficient TCAM
Low activity
Voltage Overscaling
Accuracy!
Imani, DATE’16
Imani, ISQED’16
Rahimi, DATE’15
Imani, TETC’16
Imani, DATE’16
NVM TCAM
Guo ISCA’13
Yavits TACO’14
Sharad DAC’13
Zhang DAET’15

## Slide 6: Base GPU Architecture for Approximate Design
AMD Radeon HD 7970 device from Southern Islands family
  32 compute units
    4 SIMD units
      16 stream cores (parallel lanes)
2048 stream cores per device
Thermal design power: 300W!
Local Memory
Wavefront Scheduler
Compute Unit
SIMD Unit 1
SIMD Unit 2
SIMD Unit 3
SIMD Unit 4
Ultra-threaded Dispatcher
Compute Unit 1
Compute Unit 32
Global Memory
Compute Device
…
IF/ID
Vector/Scalar RF
SIMD Unit
Stream Core 16
Stream Core 1
Stream Core 2
Stream Core 3
…
Floating Point Units
Integer Units

## Slide 7: Associative Memory Integration
Notes: We add MASC within each floating point unit; it consists of TCAM and 1t-1r memory. If data is found in MASC TCAM, we clock gate the CPU. The search is done in 1 cycle of FPU.

## Slide 8: Framework of Proposed Online Profiling
Machine learning: finds the image of interest from input dataset based on pixel similarities (most represented data)
Approximate concurrent state machine: profile the selected images of interest approximately by keeping track of the number of repeated computation
Associative memory: reduce the redundant computations beside processor cores

## Slide 9: Online Learning Algorithm
Temporal difference (TD) learning
TD-LRU maintains states, representing image groups of interest
is the reword value for the pixel similarity
balances the impact of the obtained reward
TD-LRU considers the images with less than a threshold reward as non-seen images

## Slide 10: TD-LRU Learning
Image 2
Image 4
Image 3
Image 1
Image 5
Image M
Input Image
Pixel Similarity
0.3
0.5
0.1
0.9
0.5
0.2
:
Tacc=0.35
+1
+1
Reset 0
Reset 0
Reset 0
+1
:
Tnew=10

## Slide 11: TD-LRU Learning
If top K states change, we start approximate profiling
The allocated of associative memory from each state :
For example: will take 2x more number of rows than those of another image state with .

## Slide 12: Approximate Profiler
Profiler identifies frequent operand patterns in an approximated manner
Minimize the profiling overhead at the expense of the accuracy
Concurrent state machine: exploits a bloom filter, implemented with k hash functions to generate an input signature (m-bits vector)
False positive error: define as a number of operands might have a same signature value
f = (1-e-nk/m)k
Parameters | 
n: degree of memberships | No control
m: vector size | Larger  accuracy  Energy 
k: number of hash functions | Larger  accuracy  Energy 

## Slide 13: Approximate Profiler
Generate 60K different signatures of 128-bit length, we can profile the frequency pattern operands
5x lower memory space than the exact profiling case.
Acceptable error rate of 5.3%

## Slide 14: Experimental Setup
AMD GPUs
  Multi2Sim for AMD Southern Islands GPU, Radeon HD 7970 device
  OpenCL applications: Sobel, Robert, Sharpen, Shift
FPU ASIC flow
  Balanced FPUs generated by FloPoCo
  Synthesized and mapped using a 45-nm TSMC
  Optimized for power and a clock period based on TCAM delay:
    Synopsys Design Compiler
    FPU power estimation: Synopsys PrimeTime (1.0V)
ACAM design flow
  Transistor-level HSPICE simulations for power and delay using 5T-4MTJ TCAM cell [Hanyu, DATE’15]
Notes: CELL!!!!!!!!!!!!!!!

## Slide 15: Results: GPU Energy Consumption
  Trade-off between FPU and TCAM energy consumption
  Minimum point: tradeoff between FPU and TCAM consumption
  Energy saving compared to GPU alone:
Hit Rate 
FPU Energy 
TCAM Energy 

## Slide 16: Hit Rate Comparasion Offline/Online
Offline Profiling: sampling data based on the offline observation  cannot identify the proper images to be profiled  low hit rate
Online profiling: adaptively update pre-stored the TCAM values in time by considering the data locality.
Frequent profiling until the selected images are good-enough to represent the dataset

## Slide 17: Hit Rate & Energy Saving Comparison
The learning and profiling energy is fixed (in fix dataset)
Minimum energy is in small TCAM  thus online learning is important!
ACAM saves 2.9x more energy on average than offline profiling
GPU + Online ACAM | 35%
GPU + Offline ACAM | 12%
Average energy saving over 4 applications

## Slide 18: Energy in Different Dataset Size
Small dataset:
  Low hit rate difference of online and offline techniques
  Offline technique overtaken in energy saving due to zero profiling energy
  Large dataset:
  Offline profiling cannot find high-frequency patterns  low ACAM hit rate
  Online learning adaptive update the TCAM based on the temporal locality
 | Online profiling: 3.3x higher energy saving over 4 applications

## Slide 19: ACAM Robustness to Dataset
GPGPU energy difference metric for the random and locality dataset cases
Online learning makes better decisions for image selections based on the locality
Online learning still outperforms 2.1x over offline profiling
 | Dataset size |  |  |  |  | 
 | 100 | 500 | 1000 | 2000 | 3000 | 4000
Robert | 0.04 | 0.04 | 0.07 | 0.09 | 0.11 | 0.13
Sobel | 0.02 | 0.06 | 0.13 | 0.15 | 0.16 | 0.18
Sharpen | 0.05 | 0.08 | 0.14 | 0.17 | 0.19 | 0.21
Shift | 0.04 | 0.05 | 0.09 | 0.11 | 0.12 | 0.14
Energy difference increase

## Slide 20: Quality Comparison
Robert Application

## Slide 21: Conclusion
Associative memory exploits data locality to reduce the redundant computations
For IoT workload with large dataset, it is essential to use online profiling.
Our framework learns the workload and dramatically update the ACAM values based on recent represented data.
  35% GPGPU energy savings on average
  3.3X lower search energy consumption vs. state-of-the-art techniques.