## Slide 1: Brain-Inspired Computing Exploiting Carbon Nanotube FETs and Resistive RAM: Hyperdimensional Computing Case Study
T. F. Wu, H. Li, P.-C. Huang, A. Rahimi,
J. M. Rabaey, H.-S. P. Wong, M. M. Shulaker, S. Mitra

## Slide 2: Human Cognition: Unparalleled
Simple cognitive tasks for humans:
...
strategic
planning
extremely challenging for computing systems
understanding
audio/video
real-time decision making
detecting
problems

## Slide 3: Brain-Inspired Computing Systems
high promise, major disconnect vs. human brain
Computing Models ?
Chip Realization Challenges
*[Voytek Scitable 13]
billions of neurons
trillions of synapses*
Hyperdimesional (HD) computing
Convolutional neural networks
Long short-term memory
...
Compute + memory immersed on-chip
Ultra-dense connectivity
Energy-efficiency
Small footprint
...

## Slide 4: 3D Nanosystem for HD Computing
1,952 CNFETs
RRAM
CNFETs
Monolithic 3D integration, carbon nanotube FETs, resistive RAM
224 RRAM cells
Monolithic 3D

## Slide 5: 3D Nanosystem for HD Computing
Resistive RAM (RRAM) for memory and compute
RRAM
224 RRAM cells

## Slide 6: 3D Nanosystem for HD Computing
Monolithic 3D integration
Fine-grained access between computation and memory
RRAM

## Slide 7: 3D Nanosystem for HD Computing
RRAM
CNFETs
Energy-efficient carbon nanotube FETs (CNFETs)
1,952 CNFETs

## Slide 8: Key Message
Monolithic 3D nanosystem for HD computing
  Measured 98% accuracy for language classification
CNFET, RRAM, monolithic 3D overcome realization challenges
  Low-temperature fabrication key
Exploit native nanotechnology properties for HD
  Inherent variations, RRAM analog accumulator, error resilient
Live demo yesterday

## Slide 9: Hyperdimensional (HD) Nanosystem for Language Classification
21 European languages
English vs Spanish
Italian vs Dutch
Estonian vs Italian etc.
  Pairwise classification
  One-shot learning
  Measured: 98% accuracy (resilient to stuck-at faults)
100k characters per language
The brave men, living and dead, who struggled here, have consecrated it far above our poor power to add or detract.
Test sentences
  HD vector for Spanish
  HD vector for Dutch
  HD vector for Italian
….
HD nanosystem
Training text
~100 characters per sentence

## Slide 10: HD Computing: Mapping Phase
a
b
c
_
11
0
0
.
.
.
0
1
1
1
0
0
0
.
.
.
0
1
0
0
1
0
0
.
.
.
1
0
1
0
0
0
0
.
.
.
1
1
1
……
……
Hyperdimensional (HD) vectors

## Slide 11: HD Computing: Mapping Phase
a
b
c
_
11
0
0
.
.
.
0
1
1
1
0
0
0
.
.
.
0
1
0
0
1
0
0
.
.
.
1
0
1
0
0
0
0
.
.
.
1
1
1
……
……
Hyperdimensional (HD) vectors
Random projection
  Alphabet  27 HD vectors
High dimensionality: ~kbits
  Resilient to errors

## Slide 12: HD Computing: Training Phase
h
e
l
l
o
0
1
1
0
.
.
.
1
1
1
1
0
1
0
.
.
.
0
1
0
1
1
1
0
.
.
.
0
0
1
0
0
0
1
.
.
.
0
1
1
1
1
1
0
.
.
.
0
0
1
…………
English text sample

## Slide 13: HD Computing: Training Phase
h
e
l
l
o
0
1
1
0
.
.
.
1
1
1
1
0
1
0
.
.
.
0
1
0
1
1
1
0
.
.
.
0
0
1
0
0
0
1
.
.
.
0
1
1
1
1
1
0
.
.
.
0
0
1
…………
Training text: English
Multiply: Bitwise XOR
Accumulation
Permute: Circular Shift
HD Encoder
0
1
0
0
.
.
.
0
0
1
Classifier
Memory
HD Vector: entire English language
Store in

## Slide 14: HD Computing: Training Phase
h
o
l
a
_
0
1
1
0
.
.
.
1
1
1
0
0
0
1
.
.
.
0
1
1
1
1
1
0
.
.
.
0
0
1
1
0
1
1
.
.
.
0
0
1
1
1
1
1
.
.
.
0
0
0
…………
Training text: Spanish
Multiply: Bitwise XOR
Accumulation
Permute: Circular Shift
HD Encoder
1
1
0
1
.
.
.
0
1
1
HD Vector: entire Spanish language
Classifier
Memory
Store in

## Slide 15: HD Computing: Training Phase
c
i
a
o
_
0
1
1
1
.
.
.
1
0
1
0
1
0
1
.
.
.
0
0
0
1
1
1
1
.
.
.
0
0
0
1
0
1
1
.
.
.
0
0
1
0
0
0
1
.
.
.
0
1
1
…………
Training text: Italian
Multiply: Bitwise XOR
Accumulation
Permute: Circular Shift
HD Encoder
0
1
0
0
.
.
.
0
1
0
HD Vector: entire Italian language
Classifier
Memory
Store in

## Slide 16: HD Computing: Training Phase
h
a
l
o
_
0
1
1
0
.
.
.
1
1
1
1
1
1
1
.
.
.
0
0
0
1
1
1
0
.
.
.
0
0
1
1
0
1
1
.
.
.
0
0
1
0
0
0
1
.
.
.
0
1
1
…………
Training text: German
Multiply: Bitwise XOR
Accumulation
Permute: Circular Shift
HD Encoder
1
0
0
1
.
.
.
1
1
0
HD Vector: entire German language
Classifier
Memory
Store in

## Slide 17: HD Computing: Inference Phase
b
r
a
i
n
1
0
0
0
.
.
.
0
1
0
1
1
1
0
.
.
.
1
1
0
11
0
0
.
.
.
0
1
1
0
0
1
1
.
.
.
1
1
1
1
0
1
0
.
.
.
0
0
0
0
1
0
0
.
.
.
0
0
1
…………
HD Vector for English
HD Vector for Spanish
HD Encoder
Test sentence: infer language
Multiply: Bitwise XOR
Accumulation
Permute: Circular Shift
HD Encoder
Associative search/compare
(via Hamming distance)
Classifier Memory

## Slide 18: HD Computing: Inference Phase
b
r
a
i
n
1
0
0
0
.
.
.
0
1
0
1
1
1
0
.
.
.
1
1
0
11
0
0
.
.
.
0
1
1
0
0
1
1
.
.
.
1
1
1
1
0
1
0
.
.
.
0
0
0
0
1
0
0
.
.
.
0
0
1
…………
Multiply: Bitwise XOR
Accumulation
Permute: Circular Shift
HD Encoder
Associative search/compare
(via Hamming distance)
Classifier Memory
Test sentence: infer language
HD Vector for English
HD Vector for Spanish

## Slide 19: Inside the Box: HD MAP Kernels
Permute:
circular shift
0
1
0
1
.
.
.
0
0
1
1
0
1
0
.
.
.
0
1
0
Multiply:
bitwise XOR
0
1
0
1
.
.
.
0
0
1
0
1
1
0
.
.
.
0
1
1
0
0
1
1
.
.
.
0
1
0
Accumulate:
threshold
Threshold to binary
e.g., threshold = 3/2
1
0
1
1
.
.
.
0
0
0
1
0
0
1
.
.
.
0
1
0
0
0
1
1
.
.
.
1
0
1
2
0
2
3
.
.
.
1
1
1
1
0
1
1
.
.
.
0
0
0

## Slide 20: Carbon Nanotube FET (CNFET)
CNT
Energy Delay Product
10× benefit
full-chip case studies
[IBM, IMEC, Stanford,
other commercial]
sub- lithographic
CNT pitch
diameter:
~1-2 nm

## Slide 21: Big Promise, Major Obstacles
Metallic CNTs
Mis-positioned CNTs
Imperfection-Immune Paradigm
[VLSI Tech. 08, ISSCC 13, JSSC 14, IEDM 15]
Processing advances alone inadequate

## Slide 22: Experimental System Demonstrations
Instruction fetch
Data fetch
Arithmetic block
Write-back
2 million CNFETs
[Stanford, Nature, 2017]
1
2
3
4
5
6
7
8
3D Nanosystem
>2 million CNFETs
1
2
3
4
5
6
7
8
[Shulaker Nature 17]
[Stanford, Nature, 2013]
CNT computer
instruction fetch
data fetch
arithmetic block
write-back
[Shulaker Nature 13]

## Slide 23: 3D Integration
TSV pitch >> ILV pitch
Monolithic
Inter-layer vias (ILVs)
TSV (chip stacking)
Through silicon via
(TSV)
conventional vias for metal interconnects
e.g., 36nm for 10nm node [1]
[1] Mistry Intel 17

## Slide 24: Monolithic 3D
Low-temperature fabrication required (< 400°C)

## Slide 25: Realizing Monolithic 3D
Low-temperature fabrication: < 400°C
<200 °C
<200 °C
Logic
Memory
CNFETs
RRAM
Top Electrode
Bottom Electrode
Metal Oxide

## Slide 26: Realizing Monolithic 3D
+
+
Emerging Logic
Emerging Memory
Monolithic 3D Integration
Naturally enabled
Combine device + new architecture benefits
CNFETs
RRAM

## Slide 27: Silicon CMOS compatibility
Silicon foundry compatible
Silicon FETs or CNFETs + Inter-layer dielectric

## Slide 28: Silicon CMOS compatibility
Silicon foundry compatible
RRAM fabrication + Inter-layer dielectric

## Slide 29: Silicon CMOS compatibility
Silicon foundry compatible
Inter-layer vias

## Slide 30: Silicon CMOS compatibility
Silicon foundry compatible
CNFET logic fabrication

## Slide 31: Silicon CMOS compatibility
Silicon foundry compatible
Si-FETs or CNFETs
RRAM fabrication
+ Inter-layer dielectric
Inter-layer vias
CNFET fabrication
+ Inter-layer dielectric

## Slide 32: Chip overview: Monolithic 3D HD Nanosystem
Wafer-scale design and fabrication

## Slide 33: Chip overview: Monolithic 3D HD Nanosystem
Built entirely with CNFETs + RRAM
CNTs
CNT computing logic
Memory
Inter-layer vias
TiN
HfOx
Pt
RRAM

## Slide 34: Our system: language classification
Random Projection
HD Encoder
Classifier
Memory

## Slide 35: Language classification example
Four score and seven years ago…
Random Projection
HD Encoder
Classifier
Memory
0
1
1
0
.
.
.
1
1
1
0
0
1
1
.
.
.
1
0
0
0
1
1
0
.
.
.
1
1
1
0
0
1
1
.
.
.
1
0
0
Input characters ➔ HD vector representation generated

## Slide 36: Our system: language classification
Random Projection
HD Encoder
Classifier
Memory
Generates HD vector representing entire sentence
1
1
0
1
.
.
.
0
0
1

## Slide 37: Our system: language classification
Random Projection
HD Encoder
Classifier
Memory
Output currents: higher current indicates language
60 µA
40 µA
vs.
Spanish
English
1
1
0
1
.
.
.
0
0
1

## Slide 38: System Schematic
x32
𝛿
𝛿
S
R
Q
E
D
Q
clk2
in
Vtop
in
out
clk
out
clk4
clk3
lang0
lang1
Vbot
clk1
row 1 of 32
...
entirely CNFETs + RRAM
Classifier Memory
Random Projection
HD Encoder

## Slide 39: System Schematic
Random Projection
HD Encoder
Classifier Memory
row 1 of 32
...
entirely CNFETs + RRAM

## Slide 40: Monolithic 3D Library Cells: CNFETs + RRAM
Random Projection
HD Encoder
Classifier Memory
Delay Cells
Accumulator
Vb
in
out
VDD
Pgrm
RRAM
lang0
lang1
Vtop
RRAM
Vbot
Vb
VDD
Vb
VDD
VDD
Vb
clk4
in
out
row 1 of 32
...
Layer 1
Layer 2
Layer 1
Layer 2
Layer 1
Layer 2
TCAM Memory Cells

## Slide 41: Monolithic 3D Library Cells: 1 of 3
entirely CNFETs + RRAM
Random Projection
HD Encoder
Classifier Memory
Delay Cells
Accumulator
Vb
in
out
VDD
Pgrm
RRAM
lang0
lang1
Vtop
RRAM
Vbot
Vb
VDD
Vb
VDD
VDD
Vb
clk4
in
out
row 1 of 32
...
Layer 1
Layer 2
Layer 1
Layer 2
Layer 1
Layer 2
TCAM Memory Cells

## Slide 42: Random Projection utilizing variations
Variations inherent to nanotechnologies
Threshold voltage
CNT Count
Source
Drain
Source
Drain
Source
Drain
Gate
Gate
Gate
2
5
3
CNFET drive current
Filament size
Filament configuration
HfOx
RRAM resistance

## Slide 43: Random Projection utilizing variations
Delay variations lead to high HD computing accuracy
VB
In
Out
CNFET Delay Cell
VDD
Pulldown Delay
𝝻: mean delay, 𝞂: standard deviation of delays
𝛿
Chart: 
| 0.2 | 0.3 | 0.5 | 1 | 1.3 | 2
 | 74 | 80 | 90 | 95 | 97 | 98
Inference Accuracy (%)
Pulldown Delay 𝞂/𝝻
75
100

## Slide 44: Random Projection utilizing variations
CNFETs: not enough variations (small 𝞂/𝝻)
VB
In
Out
CNFET Delay Cell
VDD
Pulldown Delay
𝝻: mean delay, 𝞂: standard deviation of delays
𝛿
Chart: 
| 0.2 | 0.3 | 0.5 | 1 | 1.3 | 2
 | 74 | 80 | 90 | 95 | 97 | 98
Inference Accuracy (%)
Pulldown Delay 𝞂/𝝻
75
100
0.3
CNFET Only

## Slide 45: Random Projection utilizing variations
RRAM variations: more than CNFETs
In
Out
RRAM Delay Cell
VDD
𝝻: mean delay, 𝞂: standard deviation of delays
RRAM
𝛿
Pulldown Delay
Chart: 
| 0.2 | 0.3 | 0.5 | 1 | 1.3 | 2
 | 74 | 80 | 90 | 95 | 97 | 98
Inference Accuracy (%)
Pulldown Delay 𝞂/𝝻
75
100
0.8
RRAM Only

## Slide 46: Engineering Variations
Chart: 
| 0.2 | 0.3 | 0.5 | 1 | 1.3 | 2
 | 74 | 80 | 90 | 95 | 97 | 98
Inference Accuracy (%)
Pulldown Delay 𝞂/𝝻
75
100
VB
In
Out
VDD
Pgrm
RRAM
RRAM
CNFETs
CNFET + RRAM Delay Cell
Our implementation: VDD = 3V
1.5
CNFET + RRAM
CNFET + RRAM variations combined: largest 𝞂/𝝻
𝝻: mean delay, 𝞂: standard deviation of delays
𝛿

## Slide 47: Monolithic 3D Library Cells: 2 of 3
Random Projection
HD Encoder
Classifier Memory
Delay Cells
Accumulator
entirely CNFETs + RRAM
row 1
of 32
...
Vb
in
out
VDD
Pgrm
RRAM
lang0
lang1
Vtop
RRAM
Vbot
Vb
VDD
Vb
VDD
VDD
Vb
clk4
in
out
Layer 1
Layer 2
Layer 1
Layer 2
Layer 1
Layer 2
TCAM Memory Cells

## Slide 48: HD accumulator design
30X fewer transistors vs digital accumulator
7-bit digital accumulator (needed for HD)
>270 Transistors
9 Transistors
RRAM
Analog
Accumulator

## Slide 49: RRAM analog accumulator: leveraging gradual reset
Pulses increase resistance of RRAM
Built with RRAM + CNFET Logic
in
pulse
Vtop
Vbot
Increasing resistance
Pulses
Vtop – Vbot = -2.6V
Measured Resistance
Resistance
Number of Pulses
0
50
100
104
106
108
Our implementation: VDD = 3V
If in = 1, pulse

## Slide 50
Buffer to threshold output
Vtop
Measured Accumulator
Vtop-Vbot
out (V)
clk
Time (ms)
in = 3V
Rd
Incr
Rd
Rd
Rd
Incr
Incr
Incr
Our implementation: VDD = 3V
in
Vbot
If in = 1, pulse
out
pulse
RRAM analog accumulator: leveraging gradual reset
Built with RRAM + CNFET Logic

## Slide 51: Monolithic 3D Library Cells: 3 of 3
entirely CNFETs + RRAM
row 1
of 32
...
Random Projection
HD Encoder
Classifier Memory
Delay Cells
TCAM Memory Cells
Accumulator
Vb
in
out
VDD
Pgrm
RRAM
lang0
lang1
Vtop
RRAM
Vbot
Vb
VDD
Vb
VDD
VDD
Vb
clk4
in
out
Layer 1
Layer 2
Layer 1
Layer 2
Layer 1
Layer 2

## Slide 52: Inference in HD: RRAM current-summing
Calculate Hamming distance
Closest match vs stored HD vectors
Current Summing
lang0 (English)
lang1 (Spanish)
Current Sum (µA)
lang0
QV[0]
QV[0]
QV[1]
QV[1]
Stored ‘1’
English identified
Text 1
Text 2
Spanish
identified
Measured current
0.5V
Stored ‘0’
‘0’
‘0’
RRAM
RRAM

## Slide 53: Inference in HD: RRAM current-summing
Calculate Hamming distance
Closest match vs stored HD vectors
lang0
lang1
Current Sum (µA)
Measured current
Eng v. Spa
Eng v. Deu
Eng v. Fra
Eng v. Gre
Est v. Spa
Est v. Deu
Est v. Fra
Est v. Gre
Pol v. Spa
Pol v. Deu
Pol v. Fra
Pol v. Gre
…
Current Summing
lang0
QV[0]
QV[0]
QV[1]
QV[1]
Stored ‘1’
0.5V
Stored ‘0’
‘0’
‘0’
RRAM
RRAM

## Slide 54: Measured Language Classification Results
Pairwise classification of 21 European languages*
Mean Accuracy (%)
Chart: HD Vector Dimension
| 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192
Software | 95.7 | 97.7 | 98.65 | 99.01 | 99.22 | 99.38 | 99.38
This Work | 76 | 83.68 | 88.13 | 90.62 | 95.79 | 97.02 | 98.19
Software
Measured using our nanosystem
98%
99.2%
*Koehn, Europarl Dataset, http://www.statmt.org/europarl/, 2005.

## Slide 55: Comparison to State of the Art
CNFET demos
RRAM demos
3D Nano-
system
[Shulaker
Nature 17]
CNT Computer
[Shulaker Nature 13]
Sensor-to-Digital Interface
[Shulaker ISSCC 13]
4-bit CMOS adder
[Yang ACS
Nano 17]
Brain-inspired
3D RRAM
[Li VLSI Tech 17]
32 Gb array
[Liu JSSC 14]
Variations Utilized
This
Work
Si PUF [Alvarez ISSCC 15]
Si PUF [Yang ISSCC 15]
RRAM FPGA
[Liauw ISSCC 12]
…
…
…
…
…
…
CNT PUF
Simulation
[Konigsmark
ASP-DAC 14]

## Slide 56: Simulated HD Computing Projections
35X less EDP, 3X smaller area
Simulated 28nm Silicon
Simulated 28nm Monolithic 3D
3 Tiers
Silicon FETs + Silicon SRAM
CNFETs + RRAM
Random projection: SRAM lookup
Classifier Mem.: SRAM TCAM
Digital accumulators
Classifier Mem.: CNFET+RRAM TCAM
RRAM analog accumulators
Random projection: Delay cells
Post place-and-route area and energy-delay product (EDP), HV dimension 10,000 bits

## Slide 57: Simulated HD Computing Projections
Simulations show major benefits
Chart: 
| Silicon | Monolithic 3D
Classify | 0.09 | 0.0041804
Projection | 0.3 | 0.013848
Encoding | 0.61 | 0.11235
Chart: 
| Silicon | Monolithic 3D
Classify | 0.007874 | 0.0017288
Projection
Encoding | 0.99213 | 0.21783
4.6X
7.6X
Post place-and-route area and energy-delay product (EDP), HV dimension 10,000 bits
Execution Time
Energy

## Slide 58: Key Message
Monolithic 3D nanosystem for HD computing
  Measured 98% accuracy for language classification
CNFET, RRAM, monolithic 3D overcome realization challenges
  Low-temperature fabrication key
Exploit native nanotechnology properties for HD
  Inherent variations, RRAM analog accumulator, error resilient

## Slide 59: Live demo yesterday
10µm
Random Projection
HD Classifier
HD Encoder
User text input
Statistics display
Gumball visualization
CNFET + RRAM Chip

## Slide 60: Acknowledgments

## Slide 61: Key Message
Monolithic 3D nanosystem for HD computing
  Measured 98% accuracy for language classification
CNFET, RRAM, monolithic 3D overcome realization challenges
  Low-temperature fabrication key
Exploit native nanotechnology properties for HD
  Inherent variations, RRAM analog accumulator, error resilient
Live demo yesterday