## Slide 1
Supervised Learning Based Model for Predicting Variability-Induced Timing Errors
Xun Jiao, Abbas Rahimi, Balakrishnan Narayanaswamy, Hamed Fatemi, Jose Pineda de Gyvez, Rajesh K. Gupta UCSD, NXP Semiconductors

## Slide 2: Outline
Motivation
  Variability causes timing errors
Timing error analysis framework
Prediction model based on supervised learning
  Supervised learning method
  History notion
  Per-stage vs. per-operator
Experimental result
  Prediction accuracy
  Guardband reduction on approximate applications
Conclusion and future work

## Slide 3: Outline
Motivation
  Variability causes timing errors
Timing error analysis framework
Prediction model based on supervised learning
  Supervised learning method
  History notion
  Per-stage vs. per-operator
Experimental result
  Prediction accuracy
  Guardband reduction on approximate applications
Conclusion and future work

## Slide 4: Variability Causes Timing Errors
Temperature
Clock
actual circuit delay
guardband
Aging
VCC Droop
Process
Sources of variations: manufacturing, environmental and workload  timing errors in hardware
Avoiding timing errors  Conservative guardbands  Efficiency loss 

## Slide 5: Guardband Reduction Techniques
Detection & Correction : Observation using in situ monitors (Razor, EDS) with cycle-by-cycle corrections (leveraging CMOS knobs or replay)
Predict & Prevent : Relying on external or replica monitors Model-based rule  derive adaptive guardband to prevent error
Error acceptance: Accepting errors in approximate applications while ensuring application quality
Detect
Correct
Sensor
Model
Prevent
[1] Abbas Rahimi, et al., “Hierarchically Focused Guardbanding: An Adaptive Approach to Mitigate PVT Variations and Aging,” DATE2013.
Quality
Approximate
Prediction & Prevention + Error acceptance

## Slide 6: Our Contributions
Predicting bit-level timing error for unseen workload, while
  Varying voltage and temperature corners
  Varying clock speed
We use a supervised learning method that exhibits an average prediction accuracy of 95% for different FPUs
This accuracy can be used to achieve a 0%–15% guardband reduction
  While satisfying the reliability specification for four error-tolerant applications
Supervised learning methods for timing error model generation, such as ours, can open the doors for online guardband management!

## Slide 7: Outline
Motivation
  Variability causes timing errors
Timing error analysis framework
Prediction model based on supervised learning
  Supervised learning method
  History notion
  Per-stage vs. per-operator
Experimental result
  Prediction accuracy
  Guardband reduction on approximate applications
Conclusion and future work

## Slide 8: Timing Error Extraction and Model Validation Flow
Error Prediction
Trained Prediction Model
Applications
Validation
Prediction Accuracy & Skill Score
Profiling Data
45nm Cell Libs
Design
Compiler
IC Compiler
FPUs VHDL
Prime
Time
Variable
Parameters
Netlist &SPEF
(Voltage,
Temp)
Clock
ModelSim Simulation
STA
FloPoCo
Golden Output
ASIC flow
  RTL from FloPoCo
  Placed-and-routed
  TSMC 45nm
Gate-level simulation
  SDF back-annotation
  Varying clock speed and inputs
Model validation
  Profiling data from Multi2Sim
  Comparison between prediction result and golden result

## Slide 9: Outline
Motivation
  Variability causes timing errors
Timing error analysis framework
Prediction model based on supervised learning
  Supervised learning method
  History notion
  Per-stage vs. per-operator
Experimental result
  Prediction accuracy
  Guardband reduction on approximate applications
Conclusion and future work

## Slide 10: Supervised Learning
Why supervised learning for model generation?
*
a [31:0]
b [31:0]
CLK
M1
Mi
…
c [31:0]
Binary classifier: Given any input features, predict whether some bit would be erroneous.
Evaluate three different methods: K-NN, SVM and LR.
K-NN: less than 80% prediction accuracy 
SVM vs. LR: Equal high prediction accuracy 
LR has better efficacy in the training time!
LR: For input x we predict timing erroneous if
where

## Slide 11: Capturing History for Inputs
Binary classifier
Input feature
Output target
Data stream
Output at each cycle
Corresponding input???
op1 op2
Ci: 0011 1101
Ci+1 : 0101 1010
Ci+2 : 1100 0110
output
Ci+6 : 01xx
Ci+7 : x101
Ci+8 : 0x1x
6 stage pipeline delay
op1 op2
Ci+100: 0101 1001
Ci+101 : 0101 1010
Ci+102 : 1100 0110
output
Ci+106 : 01xx
Ci+107 : 1x0x
Ci+108 : 0x1x
6 stage pipeline delay
Hamming distance: 3
Corresponding input: combine previous input and current input {x[t], x[t+1]}
Hamming distance: 0

## Slide 12: Modeling Strategies: Per-stage vs. Per-FPU
*
a [31:0]
b [31:0]
CLK
M1
Mi
…
c [31:0]
model
model
model
model
Per-stage: build model for each stage and then combine them together
Per-FPU: build model for entire FPU.
0.1% difference between two granularity.
Per-FPU is more computational efficient.

## Slide 13: Model Generation and Model Utilization
(V, T, Clock)
Training
Inputs
Delay
Simulation
Golden Output
Prediction Model Using Binary Classifiers
Xt-1
Xt
Yt
Model Generation
Test
Inputs
Delay
(V, T)
X’t-1
X’t
Possible Guardband Reduction
Model Utilization
Reliability Specification
Prediction Model Using Binary Classifiers
Clock

## Slide 14: Outline
Motivation
  Variability causes timing errors
Timing error analysis framework
Prediction model based on supervised learning
  Supervised learning method
  History notion
  Per-stage vs. per-operator
Experimental result
  Prediction accuracy
  Guardband reduction on approximate applications
Conclusion and future work

## Slide 15: Reliability Specification for Approximate Computing
Image processing applications: Sobel and Gaussian filters (PSNR > 26dB)
Other applications: Matrix Multiplication, DCT (Deviation < 10%)
Sobel filter: Adder, Multiplier and SQRT
Reference
PSNR=30dB
Approximation
Reliability specification: The probability that a bit must keep reliable to make the output quality acceptable.
Errors in 20th bit in the multiplier with probability of 0.2  PSNR of 34dB.  reliability speciﬁcation(20th bit) < 80%.
Chart: bit position
| 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
 | 0 | 0.75 | 0.9 | 0.97 | 0.99 | 0.998 | 0.998 | 0.999 | 0.9993 | 0.9995 | 0.9998 | 0.9999 | 0.9995

## Slide 16: Our Goal
Prediction accuracy > reliability specification  guardband reduction

## Slide 17: Prediction Accuracy
Prediction accuracy (minimum, average, maximum) at two corners.
Chart: bit position
| 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
 | 0 | 0.75 | 0.9 | 0.97 | 0.99 | 0.998 | 0.998 | 0.999 | 0.9993 | 0.9995 | 0.9998 | 0.9999 | 0.9995
 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
 | 1 | 0.9999 | 0.9999 | 0.9999 | 0.9999 | 1 | 1 | 1 | 1 | 1 | 1 | 0.9998 | 1
 | 0.9944 | 0.9967 | 0.9989 | 0.9995 | 1 | 0.9995 | 0.9996 | 0.9997 | 0.9997 | 0.9997 | 0.9997 | 0.9996 | 1
Chart: bit position
| 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
 | 0 | 0.1 | 0.8 | 0.95 | 0.98 | 0.996 | 0.997 | 0.998 | 0.998 | 0.999 | 0.999 | 0.9998 | 0.9998 | 0.999
 | 0.9986 | 0.9984 | 0.9983 | 0.9992 | 0.9984 | 0.9982 | 0.9983 | 0.9982 | 0.9984 | 0.9985 | 0.9987 | 0.9987 | 0.9987 | 1
 | 0.9924 | 0.9912 | 0.9909 | 0.9954 | 0.9887 | 0.9903 | 0.9906 | 0.9928 | 0.9948 | 0.9955 | 0.9957 | 0.9957 | 0.9961 | 0.9994
 | 0.9818 | 0.982 | 0.9902 | 0.9857 | 0.9699 | 0.9807 | 0.9896 | 0.9868 | 0.9891 | 0.9896 | 0.9926 | 0.9937 | 0.978 | 0.9984
Chart: bit position
| 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
Reliability specification | 0 | 0.8 | 0.9 | 0.93 | 0.95 | 0.97 | 0.98 | 0.98 | 0.98 | 0.99
5% GBR prediction accuracy | 0.9993 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
10% GBR prediction accuracy | 0.9994 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
15% GBR prediction accuracy | 0.996 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Multiplier
Adder
SQRT
Reliability specification and prediction accuracy for Sobel filter at (0.85V, 50C).
Notes: Emphasize prediction accuracy > reliability spec

## Slide 18: Guardband Reduction
Bit-level guardband reduction (%) for the multiplier at two corners: (0.72V, 0◦C)/(0.85V, 50◦C).
Bit-level guardband reduction (%) for the adder at two corners: (0.72V, 0◦C)/(0.85V, 50◦C).
Instruction-level guardband reduction (%) at two corners: (0.72V, 0◦C)/(0.85V, 50◦C).

## Slide 19: Conclusion
Generates a functional model for predicting the timing errors at the bit-level for a given amount of reduced guardband.
An average accuracy of 95% for timing error prediction with a wide range of variability conditions: △V=0.13V and △T=50°C and unseen workload.
The guardband can be reduced 0%–15% while satisfying the reliability specification for the error-tolerant applications.
Future work
  Our ongoing work focuses on efficient utilization of such modeling approach for runtime guardband reduction